## Slide 1: GPU Performance Analysis and Optimization
Paulius Micikevicius
Developer Technology, NVIDIA
2017.04.06
Jinsu Lee
Notes: Thank you, Mr. Chairman.
Good morning. I’m Gyeonghoon Kim from KAIST in Korea.
Today I’d like to talk about “A Low-energy Hybrid Radix-4/-8 Multiplier for Portable Multimedia Applications”.

## Slide 2: Contents
Exposing Sufficient Parallelism
Global Memory Access
Shared Memory
Arithmetic Optimizations

## Slide 3: Parallelism Needed
GPU is a parallel machine
  Lots of arithmetic pipelines
  Multiple memory banks
To get good performance, your code must expose sufficient parallelism for 2 reasons:
  To actually give work to all the pipelines
  To hide latency of the pipelines
Rough rule of thumb for K20x:
  You want to have 14K or more threads running concurrently
Exposing Sufficient Parallelism

## Slide 4: Exposing Sufficient Parallelism
What hardware ultimately needs:
  Arithmetic pipes:
    sufficient number of independent instructions
      accommodates multi-issue and latency hiding
  Memory system:
    sufficient requests in flight to saturate bandwidth
Two ways to increase parallelism:
  More independent work within a thread
    ILP for math, independent accesses for memory
  More concurrent threads
Exposing Sufficient Parallelism

## Slide 5: Occupancy and Performance
Occupancy: number of concurrent threads per SM
Note that 100% occupancy isn’t needed to reach maximum performance
  Once the “needed” occupancy is reached, further increases won’t improve performance
Needed occupancy depends on the code
  More independent work per thread -> less occupancy is needed
  Memory-bound codes tend to need more occupancy
    Higher latency than for arithmetic, need more work to hide it
Exposing Sufficient Parallelism

## Slide 6: Kepler Memory Hierarchy
Global memory access

## Slide 7: Global Memory Operation
Memory operations are executed per warp
  32 threads in a warp provide memory addresses
  Hardware determines into which lines those addresses fall
    Memory transaction size is 32 bytes
    There are benefits to a warp accessing a contiguous aligned region of 128 or 256 bytes
Access word size
  Natively supported sizes (per thread): 1, 2, 4, 8, 16 bytes
Global memory access

## Slide 8: Scenario
Scenario:
  Warp requests 32 aligned, consecutive 4-byte words
Addresses fall within 4 segments
  Warp needs 128 bytes
  128 bytes move across the bus
  Bus utilization: 100%
Global memory access

## Slide 9: Scenario
Scenario:
  Warp requests 32 aligned, permuted 4-byte words
Addresses fall within 4 segments
  Warp needs 128 bytes
  128 bytes move across the bus
  Bus utilization: 100%
Global memory access

## Slide 10: Scenario
Scenario:
  Warp requests 32 misaligned, consecutive 4-byte words
Addresses fall within at most 5 segments
  Warp needs 128 bytes
  At most 160 bytes move across the bus
  Bus utilization: at least 80%
    Some misaligned patterns will fall within 4 segments, so 100% utilization
Global memory access

## Slide 11: Scenario
Scenario:
  All threads in a warp request the same 4-byte word
Addresses fall within a single segment
  Warp needs 4 bytes
  32 bytes move across the bus
  Bus utilization: 12.5%
Global memory access

## Slide 12: Scenario
Scenario:
  Warp requests 32 scattered 4-byte words
Addresses fall within N segments
  Warp needs 128 bytes
  N*32 bytes move across the bus
  Bus utilization: 128 / (N*32)
Global memory access

## Slide 13: Structure of Non-Native Size
Say we are reading a 12-byte structure per thread
  struct Position
  {
  float x, y, z;
  };
  ...
  __global__ void kernel( Position *data, ... )
  {
  int idx = blockIdx.x * blockDim.x + threadIdx.x;
  Position temp = data[idx];
  ...
  }
Global memory access

## Slide 14: Structure of Non-Native Size
First Load Instruction
Second Load Instruction
Third Load Instruction
Global memory access

## Slide 15: Solutions
Moving 3x more bytes than application requests
Change data layout from array of structures to structure of arrays
  In this case: 3 separate arrays of floats
  The most reliable approach (also ideal for both CPUs and GPUs)
Use loads via read-only cache
  As long as lines survive in the cache, performance will be nearly optimal
Stage loads via shared memory
Global memory access

## Slide 16: Shared Memory
On-chip (on each SM) memory
Comparing SMEM to GMEM:
  Order of magnitude (20-30x) lower latency
  Order of magnitude (~10x) higher bandwidth
  Accessed at bank-width granularity
Shared memory

## Slide 17: Shared Memory Bank Conflicts
A bank conflict occurs when:
  2 or more threads in a warp access different words in the same bank
  N-way bank conflict: N threads in a warp conflict
Note there is no bank conflict if:
  Several threads access the same word
  Several threads access different bytes of the same word
Shared memory

## Slide 18: SMEM Access Examples
No Bank Conflicts Cases
Shared memory

## Slide 19: SMEM Access Examples
Bank Conflicts Cases
Shared memory

## Slide 20: SMEM Access Examples
Shared memory is a tremendous resource
  Very high bandwidth (terabytes per second)
  20-30x lower latency than accessing GMEM
Performance issues to look out for:
  Bank conflicts add latency and reduce throughput
  Many-way bank conflicts can be very expensive
    Replay latency adds up
    However, few code patterns have high conflicts, padding is a very simple and effective solution
Shared memory

## Slide 21: Execution
Instructions are issued/executed per warp
  Warp = 32 consecutive threads
    Think of it as a “vector” of 32 threads
    The same instruction is issued to the entire warp
Scheduling
  Warps are scheduled at run-time
  Hardware picks from warps that have an instruction ready to execute
    Ready = all arguments are ready
  Instruction latency is hidden by executing other warps
Arithmetic optimizations

## Slide 22: Conditional Control Flow
If at least one thread in a warp needs take a particular path:
  All threads in a warp take that path
  Threads that aren’t on that path:
    Don’t fetch arguments, don’t write outputs: guarantees correctness
    Still spend time, instead of executing their path: potential performance impact
Arithmetic optimizations

## Slide 23: Control Flow
Arithmetic optimizations

## Slide 24: Execution within warps is coherent
Arithmetic optimizations

## Slide 25: Execution diverges within a warp
Arithmetic optimizations

## Slide 26: Instruction Throughput: Summary
Analyze:
  Check achieved instruction throughput
  Compare to HW peak
  Check percentage of instructions due to serialization
Optimizations:
  Intrinsics, compiler options for expensive operations
  Group threads that are likely to follow same execution path (minimize warp divergence)
  Minimize memory access replays (SMEM and GMEM)
Arithmetic optimizations