## Slide 1: GPU Performance Analysis and Optimization
Paulius Micikevicius
Developer Technology, NVIDIA

## Slide 2: Main Requirements for GPU Performance
Expose sufficient parallelism
Use memory efficiently
  Coalesce global memory access
  Use shared memory where possible
Have coherent execution within warps

## Slide 3: Exposing sufficient parallelism

## Slide 4: Parallelism Needed
GPU is a parallel machine
  Lots of arithmetic pipelines
  Multiple memory banks
To get good performance, your code must expose sufficient parallelism for 2 reasons:
  To actually give work to all the pipelines
  To hide latency of the pipelines
Rough rule of thumb for K20x:
  You want to have 14K or more threads running concurrently

## Slide 5: Exposing Sufficient Parallelism
What hardware ultimately needs:
  Arithmetic pipes:
    sufficient number of independent instructions
      accommodates multi-issue and latency hiding
  Memory system:
    sufficient requests in flight to saturate bandwidth
Two ways to increase parallelism:
  More independent work within a thread (warp)
    ILP for math, independent accesses for memory
  More concurrent threads (warps)

## Slide 6: Kepler: Level of Parallelism Needed
To saturate instruction bandwidth:
  Fp32 math: ~1.7K independent instructions per SM
  Lower for other, lower-throughput instructions
  Keep in mind that Kepler SM can track up to 2048 threads
To saturate memory bandwidth:
  100+ independent 128-byte lines per SM

## Slide 7: Memory Parallelism
Achieved Kepler memory thoughput
  As a function of the number of independent requests per SM
  Request: 128-byte line

## Slide 8: Occupancy
Occupancy: number of concurrent threads per SM
  Expressed as either:
    the number of threads (or warps),
    percentage of maximum threads
Determined by several factors
  (refer to Occupancy Calculator, CUDA Programming Guide for full details)
  Registers per thread
    SM registers are partitioned among the threads
  Shared memory per threadblock
    SM shared memory is partitioned among the blocks
  Threads per threadblock
    Threads are allocated at threadblock granularity
Kepler SM resources
64K 32-bit registers
Up to 48 KB of shared memory
Up to 2048 concurrent threads
Up to 16 concurrent threadblocks

## Slide 9: Occupancy and Performance
Note that 100% occupancy isn’t needed to reach maximum performance
  Once the “needed” occupancy is reached, further increases won’t improve performance
Needed occupancy depends on the code
  More independent work per thread -> less occupancy is needed
  Memory-bound codes tend to need more occupancy
    Higher latency than for arithmetic, need more work to hide it

## Slide 10: Threadblock Size and Occupancy
Threadblock size is a multiple of warp size (32)
  Even if you request fewer threads, HW rounds up
Threadblocks can be too small
  Kepler SM can run up to 16 threadblocks concurrently
  SM may reach the block limit before reaching good occupancy
    Example: 1-warp blocks -> 16 warps per Kepler SM (probably not enough)
Threadblocks can be too big
  Quantization effect:
    Enough SM resources for more threads, not enough for another large block
    A threadblock isn’t started until resources are available for all of its threads

## Slide 11: Threadblock Sizing
SM resources:
  Registers
  Shared memory
Number of warps allowed by SM resources
Too few threads per block
Too many threads per block

## Slide 12: General Guidelines
Threadblock size choice:
  Start with 128-256 threads per block
    Adjust up/down by what best matches your function
    Example: stencil codes prefer larger blocks to minimize halos
  Multiple of warp size (32 threads)
  If occupancy is critical to performance:
    Check that block size isn’t precluding occupancy allowed by register and SMEM resources
Grid size:
  1,000 or more threadblocks
    10s of waves of threadblocks: no need to think about tail effect
      See GTC12 talk on optimization for more details on tails
    Makes your code ready for several generations of future GPUs

## Slide 13: General Guidelines
Concurrent grids
  Useful if any one given function doesn’t expose enough parallelism to saturate the GPU
  Math pipes and memory system don’t really care where the work is coming from, as long as there’s enough of it
Two cases:
  Concurrent grids from the same CPU process
    Launch different functions into different streams
  Several CPU processes sharing the GPU
    HyperQ feature, available on Titan

## Slide 14: Global memory access

## Slide 15: Kepler Memory Hierarchy
L2
Global Memory (DRAM)
Registers
L1
SM-1
SMEM
Read
only
Registers
L1
SM-N
SMEM
Read
only
Registers
L1
SM-0
SMEM
Read
only

## Slide 16: Memory Hierarchy Review
Registers
  Storage local to each threads
  Compiler-managed
Shared memory / L1
  64 KB, program-configurable into shared:L1
  Program-managed
  Accessible by all threads in the same threadblock
  Low latency, high bandwidth: ~2.5 TB/s
Read-only cache
  Up to 48 KB per Kepler SM
  Hardware-managed (also used by texture units)
  Used for read-only GMEM accesses (not coherent with writes)
L2
  1.5 MB
  Hardware-managed: all accesses to global memory go through L2, including CPU and peer GPU
Global memory
  6 GB, accessible by all threads, host (CPU), other GPUs in the same system
  Higher latency (400-800 cycles)
  250 GB/s

## Slide 17: Blocking for L1, Read-only, L2 Caches
Short answer: DON’T
GPU caches are not intended for the same use as CPU caches
  Smaller size (especially per thread), so not aimed at temporal reuse
  Intended to smooth out some access patterns, help with spilled registers, etc.
Usually not worth trying to cache-block like you would on CPU
  100s to 1,000s of run-time scheduled threads competing for the cache
  If it is possible to block for L1 then it’s possible block for SMEM
    Same size
    Same or higher bandwidth
    Guaranteed locality: hw will not evict behind your back

## Slide 18: Memory Throughput Analysis
Two perspectives on the throughput:
  Application’s point of view:
    count only bytes requested by application
  HW point of view:
    count all bytes moved by hardware
The two views can be different:
  Memory is accessed at 32 byte granularity
    Scattered/offset pattern: application doesn’t use all the hw transaction bytes
  Broadcast: the same small transaction serves many threads in a warp
Two aspects to inspect for performance impact:
  Address pattern
  Number of concurrent accesses in flight

## Slide 19: Global Memory Operation
Memory operations are executed per warp
  32 threads in a warp provide memory addresses
  Hardware determines into which lines those addresses fall
    Memory transaction granularity is 32 bytes
    There are benefits to a warp accessing a contiguous aligned region of 128 or 256 bytes
Access word size
  Natively supported sizes (per thread): 1, 2, 4, 8, 16 bytes
    Assumes that each thread’s address is aligned on the word size boundary
  If you are accessing a data type that’s of non-native size, compiler will generate several load or store instructions with native sizes

## Slide 20
Scenario:
  Warp requests 32 aligned, consecutive 4-byte words
Addresses fall within 4 segments
  Warp needs 128 bytes
  128 bytes move across the bus
  Bus utilization: 100%
...
addresses from a warp
96
192
128
160
224
288
256
32
64
352
320
384
448
416
Memory addresses
0

## Slide 21
...
addresses from a warp
Scenario:
  Warp requests 32 aligned, permuted 4-byte words
Addresses fall within 4 segments
  Warp needs 128 bytes
  128 bytes move across the bus
  Bus utilization: 100%
96
192
128
160
224
288
256
32
64
352
320
384
448
416
Memory addresses
0

## Slide 22
Scenario:
  Warp requests 32 misaligned, consecutive 4-byte words
Addresses fall within at most 5 segments
  Warp needs 128 bytes
  At most 160 bytes move across the bus
  Bus utilization: at least 80%
    Some misaligned patterns will fall within 4 segments, so 100% utilization
96
192
128
160
224
288
256
32
64
352
320
384
448
416
Memory addresses
0
...
addresses from a warp

## Slide 23
addresses from a warp
Scenario:
  All threads in a warp request the same 4-byte word
Addresses fall within a single segment
  Warp needs 4 bytes
  32 bytes move across the bus
  Bus utilization: 12.5%
...
96
192
128
160
224
288
256
32
64
352
320
384
448
416
Memory addresses
0

## Slide 24
addresses from a warp
96
192
128
160
224
288
256
32
64
352
320
384
448
416
Memory addresses
0
Scenario:
  Warp requests 32 scattered 4-byte words
Addresses fall within N segments
  Warp needs 128 bytes
  N*32 bytes move across the bus
  Bus utilization: 128 / (N*32)
...

## Slide 25: Structure of Non-Native Size
Say we are reading a 12-byte structure per thread
  struct Position
  {
  float x, y, z;
  };
  ...
  __global__ void kernel( Position *data, ... )
  {
  int idx = blockIdx.x * blockDim.x + threadIdx.x;
  Position temp = data[idx];
  ...
  }

## Slide 26: Structure of Non-Native Size
Compiler converts temp = data[idx] into 3 loads:
  Each loads 4 bytes
  Can’t do an 8 and a 4 byte load: 12 bytes per element means that every other element wouldn’t align the 8-byte load on 8-byte boundary
Addresses per warp for each of the loads:
  Successive threads read 4 bytes at 12-byte stride

## Slide 27: First Load Instruction
4
8
12
16
20
56
60
64
0
24
48
52
36
40
44
28
32
addresses from a warp
...

## Slide 28: Second Load Instruction
4
8
12
16
20
56
60
64
0
24
48
52
36
40
44
28
32
addresses from a warp
...

## Slide 29: Third Load Instruction
4
8
12
16
20
56
60
64
0
24
48
52
36
40
44
28
32
addresses from a warp
...

## Slide 30: Performance and Solutions
Because of the address pattern, we end up moving 3x more bytes than application requests
  We waste a lot of bandwidth, leaving performance on the table
Potential solutions:
  Change data layout from array of structures to structure of arrays
    In this case: 3 separate arrays of floats
    The most reliable approach (also ideal for both CPUs and GPUs)
  Use loads via read-only cache
    As long as lines survive in the cache, performance will be nearly optimal
  Stage loads via shared memory

## Slide 31: Read-only Loads
Go through the read-only cache
  Not coherent with writes
  Thus, addresses must not be written by the same kernel
Two ways to enable:
  Decorating pointer arguments as hints to compiler:
    Pointer of interest: const __restrict__
    All other pointer arguments: __restrict__
      Conveys to compiler that no aliasing will occur
  Using __ldg() intrinsic
    Requires no pointer decoration

## Slide 32: Read-only Loads
Go through the read-only cache
  Not coherent with writes
  Thus, addresses must not be written by the same kernel
Two ways to enable:
  Decorating pointer arguments as hints to compiler:
    Pointer of interest: __restrict__ const
    All other pointer arguments: __restrict__
      Conveys to compiler that no aliasing will occur
  Using __ldg() intrinsic
    Requires no pointer decoration
__global__ void kernel( int*__restrict__ output,
const int* __restrict__ input )
{
...
output[idx] = ... + input[idx];
}

## Slide 33: Read-only Loads
Go through the read-only cache
  Not coherent with writes
  Thus, addresses must not be written by the same kernel
Two ways to enable:
  Decorating pointer arguments as hints to compiler:
    Pointer of interest: __restrict__ const
    All other pointer arguments: __restrict__
      Conveys to compiler that no aliasing will occur
  Using __ldg() intrinsic
    Requires no pointer decoration
__global__ void kernel( int *output,
int *input )
{
...
output[idx] = ... + __ldg( &input[idx] );
}

## Slide 34: Having Sufficient Concurrent Accesses
In order to saturate memory bandwidth, SM must issue enough independent memory requests

## Slide 35: Elements per Thread and Performance
Experiment: each warp has 2 concurrent requests (memcopy, one word per thread)
  4B word request: 1 line
  8B word request: 2 lines
  16B word request: 4 lines
To achieve the same throughput at lower occupancy:
  Need more independent requests per warp
To achieve the same throughput with smaller words:
  Need more independent requests per warp

## Slide 36: Optimizing Access Concurrency
Have enough concurrent accesses to saturate the bus
  Little’s law: need (mem_latency)x(bandwidth) bytes
Ways to increase concurrent accesses:
  Increase occupancy (run more warps concurrently)
    Adjust threadblock dimensions
      To maximize occupancy at given register and smem requirements
    If occupancy is limited by registers per thread:
      Reduce register count (-maxrregcount option, or __launch_bounds__)
  Modify code to process several elements per thread
    Doubling elements per thread doubles independent accesses per thread

## Slide 37: Optimizations When Addresses Are Coalesced
When looking for more performance and code:
  Is memory bandwidth limited
  Achieves high percentage of bandwidth theory
  Addresses are coalesced
Consider compression
  GPUs provide instructions for converting between fp16, fp32, and fp64 representations:
    A single instruction, implemented in hw (__float2half(), ...)
  If data has few distinct values, consider lookup tables
    Store indices into the table
    Small enough tables will likely survive in caches if used often enough

## Slide 38: L1 Sizing
Shared memory and L1 use the same 64KB
  Program-configurable split:
    Fermi: 48:16, 16:48
    Kepler: 48:16, 16:48, 32:32
  CUDA API: cudaDeviceSetCacheConfig(), cudaFuncSetCacheConfig()
Large L1 can improve performance when:
  Spilling registers (more lines in the cache -> fewer evictions)
Large SMEM can improve performance when:
  Occupancy is limited by SMEM

## Slide 39: Summary: GMEM Optimization
Strive for perfect address coalescing per warp
  Align starting address (may require padding)
  A warp will ideally access within a contiguous region
  Avoid scattered address patterns or patterns with large strides between threads
Analyze and optimize address patterns:
  Use profiling tools (included with CUDA toolkit download)
  Compare the transactions per request to the ideal ratio
  Choose appropriate data layout (prefer SoA)
  If needed, try read-only loads, staging accesses via SMEM
Have enough concurrent accesses to saturate the bus
  Launch enough threads to maximize throughput
    Latency is hidden by switching threads (warps)
  If needed, process several elements per thread
    More concurrent loads/stores

## Slide 40: Shared memory

## Slide 41: Shared Memory
On-chip (on each SM) memory
Comparing SMEM to GMEM:
  Order of magnitude (20-30x) lower latency
  Order of magnitude (~10x) higher bandwidth
  Accessed at bank-width granularity
    Kepler: 8 bytes
    For comparison: GMEM access granularity is either 32 or 128 bytes
SMEM instruction operation:
  32 threads in a warp provide addresses
  Determine into which 8-byte words addresses fall
  Fetch the words, distribute the requested bytes among the threads
    Multi-cast capable
    Bank conflicts cause serialization

## Slide 42: Kepler Shared Memory Banking
32 banks, 8 bytes wide
  Bandwidth: 8 bytes per bank per clock per SM (256 bytes per clk per SM)
  2x the bandwidth compared to Fermi
Two modes:
  4-byte access (default):
    Maintains Fermi bank-conflict behavior exactly
    Provides 8-byte bandwidth for certain access patterns
  8-byte access:
    Some access patterns with Fermi-specific padding may incur bank conflicts
    Provides 8-byte bandwidth for all patterns (assuming 8-byte words)
  Selected with cudaDeviceSetSharedMemConfig() function arguments:
    cudaSharedMemBankSizeFourByte
    cudaSharedMemBankSizeEightByte

## Slide 43: Kepler 8-byte Bank Mode
Mapping addresses to banks:
  Successive 8-byte words go to successive banks
  Bank index:
    (8B word index) mod 32
    (4B word index) mod (32*2)
    (byte address) mod (32*8)
  Given the 8 least-significant address bits: ...BBBBBxxx
    xxx selects the byte within an 8-byte word
    BBBBB selects the bank
    Higher bits select a “column” within a bank

## Slide 44: Kepler 8-byte Bank Mode
To visualize, let’s pretend we have 4 banks, not 32 (easier to draw)
0
1
8
9
Bank-0
2
3
Bank-1
4
5
Bank-2
6
7
Bank-3
0
1
2
3
4
5
6
7
8
0
4
8
12
16
20
24
28
32
38
9
40
Data:
(or 4B-word index)
Byte-address:

## Slide 45: Shared Memory Bank Conflicts
A bank conflict occurs when:
  2 or more threads in a warp access different words in the same bank
    Think: 2 or more threads access different “rows” in the same bank
  N-way bank conflict: N threads in a warp conflict
    Instruction gets issued N times: increases latency
Note there is no bank conflict if:
  Several threads access the same word
  Several threads access different bytes of the same word

## Slide 46: SMEM Access Examples
Bank-0
Bank-1
Bank-2
Bank-31
Bank-3
Addresses from a warp: no bank conflicts
One address access per bank

## Slide 47: SMEM Access Examples
Bank-0
Bank-1
Bank-2
Bank-31
Bank-3
Addresses from a warp: no bank conflicts
One address access per bank

## Slide 48: SMEM Access Examples
Bank-0
Bank-1
Bank-2
Bank-31
Bank-3
Addresses from a warp: no bank conflicts
Multiple addresses per bank, but within the same word

## Slide 49: SMEM Access Examples
Bank-0
Bank-1
Bank-2
Bank-31
Bank-3
Addresses from a warp: 2-way bank conflict
2 accesses per bank, fall in two different words

## Slide 50: SMEM Access Examples
Bank-0
Bank-1
Bank-2
Bank-31
Bank-3
Addresses from a warp: 3-way bank conflict
4 accesses per bank, fall in 3 different words

## Slide 51: Diagnosing Bank Conflicts
Profiler counters:
  Number of instructions executed, does not include replays:
    shared_load, shared_store
  Number of replays (number of instruction issues due to bank conflicts)
    l1_shared_bank_conflict
Analysis:
  Number of replays per instruction
    l1_shared_bank_conflict / (shared_load + shared_store)
  Replays are potentially a concern because:
    Replays add latency
    Compete for issue cycles with other SMEM and GMEM operations
      Except for read-only loads, which go to different hardware
Remedy:
  Usually padding SMEM data structures resolves/reduces bank conflicts

## Slide 52: Summary: Shared Memory
Shared memory is a tremendous resource
  Very high bandwidth (terabytes per second)
  20-30x lower latency than accessing GMEM
  Data is programmer-managed, no evictions by hardware
Performance issues to look out for:
  Bank conflicts add latency and reduce throughput
  Many-way bank conflicts can be very expensive
    Replay latency adds up
    However, few code patterns have high conflicts, padding is a very simple and effective solution

## Slide 53: Arithmetic optimizations

## Slide 54: Execution
Instructions are issued/executed per warp
  Warp = 32 consecutive threads
    Think of it as a “vector” of 32 threads
    The same instruction is issued to the entire warp
Scheduling
  Warps are scheduled at run-time
  Hardware picks from warps that have an instruction ready to execute
    Ready = all arguments are ready
  Instruction latency is hidden by executing other warps

## Slide 55: Conditional Control Flow
If at least one thread in a warp needs take a particular path:
  All threads in a warp take that path
  Threads that aren’t on that path:
    Don’t fetch arguments, don’t write outputs: guarantees correctness
    Still spend time, instead of executing their path: potential performance impact

## Slide 56: Control Flow
if ( ... )
{
// then-clause
}
else
{
// else-clause
}
instructions

## Slide 57: Execution within warps is coherent
instructions / time
Warp
(“vector” of threads)
35
34
33
63
62
32
3
2
1
31
30
0
Warp
(“vector” of threads)

## Slide 58: Execution diverges within a warp
instructions / time
3
2
1
31
30
0
35
34
33
63
62
32

## Slide 59: Possible Performance Limiting Factors
Raw instruction throughput
  Know the kernel instruction mix
  fp32, fp64, int, mem, transcendentals, etc. have different throughputs
    Refer to the CUDA Programming Guide / Best Practices Guide
    Can examine assembly: use cuobjdump tool provided with CUDA toolkit
  A lot of divergence can “waste” instructions
Instruction serialization
  Occurs when threads in a warp issue the same instruction in sequence
    As opposed to the entire warp issuing the instruction at once
    Think of it as “replaying” the same instruction for different threads in a warp
  Mostly:
    Shared memory bank conflicts
    Memory accesses that result in multiple transactions (scattered address patterns)

## Slide 60: Instruction Throughput: Analysis
Compare achieved instruction throughput to HW capabilities
  Profiler reports achieved throughput as IPC (instructions per clock)
  Peak instruction throughput is documented in the Programming Guide
    Profiler also provides peak fp32 throughput for reference (doesn’t take your instruction mix into consideration)
Check for serialization
  Number of replays due to serialization: instructions_issued - instructions_executed
  Profiler reports:
    % of serialization metric (ratio or replays to instructions issued)
    Kepler: counts replays due to various memory access instructions
  A concern if: code is instruction or latency-limited, replay percentage is high
Warp divergence
  Profiler counters: divergent_branch, branch
  Compare the two to see what percentage diverges
    However, this only counts the branches, not the rest of serialized instructions

## Slide 61: Instruction Throughput: Optimization
Use intrinsics where possible ( __sin(), __sincos(), __exp(), etc.)
  Available for a number of math.h functions
  2-3 bits lower precision, much higher throughput
    Refer to the CUDA Programming Guide for details
  Often a single HW instruction, whereas a non-intrinsic is a SW sequence
Additional compiler flags that also help performance:
  -ftz=true : flush denormals to 0
  -prec-div=false : faster fp division instruction sequence (some precision loss)
  -prec-sqrt=false : faster fp sqrt instruction sequence (some precision loss)
Make sure you do fp64 arithmetic only where you mean it:
  fp64 throughput is lower than fp32
  fp literals without an “f” suffix ( 34.7 ) are interpreted as fp64 per C standard

## Slide 62: Instruction Throughput: Summary
Analyze:
  Check achieved instruction throughput
  Compare to HW peak (but keep instruction mix in mind)
  Check percentage of instructions due to serialization
Optimizations:
  Intrinsics, compiler options for expensive operations
  Group threads that are likely to follow same execution path (minimize warp divergence)
  Minimize memory access replays (SMEM and GMEM)

## Slide 63: In Conclusion
When programming and optimizing think about:
  Exposing sufficient parallelism
  Coalescing memory accesses
  Having coherent control flow within warps
Use profiling tools when analyzing performance
  Determine performance limiters first
  Diagnose memory access patterns

## Slide 64: Additional Resources
Extended version of the optimization talk:
  GTC12 Session S0514: GPU Performance Analysis and Optimization
Kepler architecture:
  GTC12 Session S0642: Inside Kepler
  Kepler whitepapers (http://www.nvidia.com/object/nvidia-kepler.html)
Assessing performance limiters:
  GTC10 Session 2012: Analysis-driven Optimization (slides 5-19):
    http://www.nvidia.com/content/GTC-2010/pdfs/2012_GTC2010v2.pdf
Profiling tools:
  GTC12 sessions:
    S0419: Optimizing Application Performance with CUDA Performance Tools
    S0420: Nsight IDE for Linux and Mac
    ...
  CUPTI documentation (describes all the profiler counters)
    Included in every CUDA toolkit (/cuda/extras/cupti/doc/Cupti_Users_Guide.pdf
Register spilling:
  Webinar:
    Slides: http://developer.download.nvidia.com/CUDA/training/register_spilling.pdf
    Video: http://developer.download.nvidia.com/CUDA/training/CUDA_LocalMemoryOptimization.mp4
GPU computing webinars in general:
  http://developer.nvidia.com/gpu-computing-webinars