## Slide 1: Lecture 7 CUDA Shared Memory
Kyu Ho Park
Mar. 28, 2017

## Slide 2
Grid
공유메모리
(Shared Memory)
Register
Block 0
Register
Thread 0
Thread 1
공유메모리
(Shared Memory)
Register
Block 1
Register
Thread 0
Thread 1
Global Memory
Constant Memory
Texture Memory
Host
CUDA Memory Architecture

## Slide 3: Shared Memory
On-board memory: Global Memory
On-chip memory: Shared memory which is smaller, faster than global memory.
The bandwidth degradation is caused by misaligned access and noncoalesced accesses of global memory.
-misaligned access: could be improved by L1 cache,
-noncoalesced access: could be improved by
shared memory.
Each SM has 64KBytes of on-chip memory which are shared by the Shared memory and L1 cache.

## Slide 4: Shared memory
Shared memory:
  An intra-block(block 내의) thread communication channel
  A program-managed cache for global memory data (can be configured by program)
  Scratch pad(small) memory for transforming data to improve global memory access patterns.
  Each SM has a shared memory which is 20~30 times faster than Global Memory.
  The shared memory address space is shared by all threads in a thread block.
  Shared memory accesses are issued per warp.
  Each request to access shared by a warp is serviced in one transaction. (individual)

## Slide 5: Transaction
Transaction processing: a processing that is divided into individual, indivisible operations.
Transaction processing:
  BEGIN_TRANACTION
  reserve Seoul-Tokyo;
  reserve Tokyo-Rio;
  reserve Rio-Bouenos;
  END_TRANSACTION
  BEGIN_TRANACTION
  reserve Seoul-Tokyo;
  reserve Tokyo-Rio;
  reserve Rio-Bouenos: NotAvailable;
  => ABORT_TRANSACTION;

## Slide 6: Shared Memory Allocation
If declared inside a kernel,
__shared__ float A[i][j];
the scope of A is local to the kernel.
If declared outside of any kernel, the scope of the variable is global to all kernels, or
extern __shared__ float B[i];

## Slide 7: CUDA Thread-block-grid
1 block can have max. 1024 threads.
SM executes threads in a multiple of 32 threads.
__global__ void kernel<<<Dg,Db,Ns,S>>>();
Dg : dimension of the grid , type dim3.
Db : dimension of the block, type dim3.
Ns : number of bytes of shared memory which are dynamically allocated/block, type size_t.
S: Associated cudaStream_t. ‘S=0 ‘ means synchronous.

## Slide 8: thread-block dimensions
dim3 Dg(3,2,1);//(x,y,z)
dim3 Db(4,2,1);//(x,y,z)
kernelFunction <<<Dg, Db>>> (a,b,c);
Grid
Block

## Slide 9: Banks of Shared Memory
Bank: the shared memory is divided into 32(=warp size) equal sized memory and they are called banks.
Bank Conflict: When multiple threads in a warp request the same bank in a shared memory. (serial access)
Memory Access Mode:
-Parallel access:
-Serial access: When multiple addresses accessed within the same bank, the request must be serialized.
-Broadcast access: All threads in a warp read the same address within a single bank. One memory access transaction is executed and the accessed word is broadcast to all requesting threads.

## Slide 10: Access Patters of Shared Memory
from [PCCP]

## Slide 11: Access Mode
Bank width:
-4 bytes for devices of compute capability 2.x,
-8 bytes for devices of compute capability 3.x.
Bank index:
bank index=(byte address/(4bytes or 8 bytes))%32

## Slide 12: Word index and Bank Index Fermi
from [PCCP]

## Slide 13: Bank index for 32-bit mode of Kepler
In Kepler device, shared memory has 32 banks with the two address mode: 32-bit mode and 64-bit mode.
from [PCCP]

## Slide 14: Bank Conflict Free Case
from [PCCP]

## Slide 15: Bank Conflict Cases
2 way conflict
3 way conflict
bank conflict가 아니다??

## Slide 16: Memory Padding
from [PCCP]
memory padding을 추가해서 bank conflict가 발생하지 않게 한다.
0으로 표시된 address을 access을 동시에 access할려면 bank conflict가 발생한다.

## Slide 17: Access Mode Configuration
cudaError_t cudaDeviceGetSharedMemConfig(cudaSharedMemConfig *pConfig);
/* The result is returned in pConfig.
The bank configuration is one of the following
cudaSharedMemBankSizeFourByte,
cudaSharedMemBankSizeEightByte. */
To set a new bank size:
cudaError_t cudaDeviceSetSharedMemConfig(cudaSharedMemConfig config);
/* The supported bank configurations:
cudaSharedMemBankSizeDefault,
cudaSharedMemBankSizeFourByte,
cudaSharedMemBankSizeEightByte */

## Slide 18: Configuring the Amount of Shared Memory
Each SM has 64KBytes of on-chip memory which are shared by the Shared memory and L1 cache.
Per-device configuration:
cudaError_t cudaDeviceSetCacheConfig(cudaFuncCache cacheConfig);
Per-kernel configuration:
cudaError_t cudaFuncSetCacheConfig(const void* func, enum cudaFuncCacheca cheConfig);

## Slide 19: Synchronization
Barrier: All calling threads wait for all other calling threads to reach the barrier points.
Memory fence: All calling threads stall until all modifications to memory are visible to all other calling threads.

## Slide 20: Weakly-Ordered Memory Model
The order of writing data to memory is not necessarily the same order of those accesses in the source codes.
The order of reading data from different memories is not necessarily the order of each read instruction in the program if instructions are independent each other.

## Slide 21: Explicit Barrier
It is possible to perform a barrier among threads in the same thread block.
void __syncthreads( );
/* it acts as a barrier point at which threads in a block must wait until all threads have reached that point.

## Slide 22: Memory Fence
It ensures that any memory write before the fence is visible to other threads after the fence.
There are three memory fences depending on
the scope:
-block: void __threadfence_block();
-grid : void __threadfence( );
-system( host and device):
void __threadfence_system( );//this one stalls the calling thread to ensure all its writes to global memory, page-locked host memory, and the memory of other devices are visible to all threads in all devices and host threads.

## Slide 23: Data Layout of Shared Memory Square Shared Memory
1D data layout
32x32 2D shared memoy layout(logical)
from [PCCP]

## Slide 24: Square shared memory
2D shared memory variable is declared statically as follows:
  __shared__ int tile[N][N];
Two ways to access the tile:
  tile[threadIdx.x][threadIdx.y]
  tile[threadIdx.y][threadIdx.x]
  Which is better?

## Slide 25
The best case is that threads in the same warp access separate banks.
Threads in the same warp can be identified by consecutive values of threadIdx.x.
tile[threadIdx.y][threadIdx.x] will show better performance and fewer bank conflicts than tile[threadIdx.x][threadIdx.y].

## Slide 26: Accessing Row-Major /Column-Major
0 (0,0) | 1 (1,0) | 2 (2,0)
3 (0,1) | 4 (1,1) | 5 (2,1)
address | thread
0 | 0
1 | 3
2 | 1
3 | 4
4 | 2
5 | 5
address | thread
0 | 0
1 | 1
2 | 2
3 | 3
4 | 4
5 | 5
Row-Major no bank conflict
Column-Major
block(3,2,1)

## Slide 27
A grid with 2D block 32 x 32:
#define BDIMX 32
#define BDIMY 32
dim3 block( BDIMX, BDIMY);
dim3 grid(1,1);
Kernel operations:
  write global thread indices to a 2D shared memory
  array in row-major order.
  read those values from shared memory in row-major order and store them to global memory.

## Slide 28: Row-Major Access
__global__ void setRowReadRow(int *out){
__shared__ int tile[BDIMY][BDIMX];
unsigned int idx=threadIdx.y*blockDimx.x+threadIdx.x;
tile[threadIdx.y][threadIdx.x]=idx;
__syncthreads();
out[idx]=tile[threadIdx.y][threadIdx.x];
}

## Slide 29: Column-Major Access
__global__ void setColReadCol(int *out){
__shared__ int tile[BDIMX][BDIMY];
unsigned int Idx=threadIdx.y*blockDim.x + threadIdx.x;
tile[threadIdx.x][threadIdx.y]=idx;
__syncthreads( );
out[idx]=tile[threadIdx.x][threadIdx.y];
}

## Slide 30: Writing Row-Major and Reading Column-Major
__global__ void setRowReadCol(int *out){
__shared__ int tile[BDIMY][BDIMX];
unsigned int idx=threadIdx.y*blockDim.x+threadIdx.x;
tile[threadIdx.y][threadIdx.x]=idx;
__syncthreads();
out[idx]=tile[threadIdx.x][threadIdx.y;;
}

## Slide 31: Writing Row-Major, Reading Column-Major
 |  | (ix,iy) | 
 | (iy,ix) |  | 
blockDim.x
-------------------------------------------------------->
Bank0 Bank1 Bank2 Bank3
Read from(ix,iy)
Write to (iy,ix)

## Slide 33: Dynamic Shared Memory
__global__ void setRowReadColDyn(int *out){
extern __shared__ int tile[];
//mapping from thread index to global memory index
unsigned int row_idx=threadIdx.y*blockDim.x + threadIdx.x;
unsigned int col_idx=threadIdx.x*blockDim.y + threadIdx.y;
//shared memory store operation
tile[row_idx]=row_idx;
__syncthreads();
//shared memory load operation
out[row_idx]=tile[col_idx];
}

## Slide 34: Padding Statically Declared Shared Memory
__global__ void setRowReadColPad(int *out) {
__shared__ int tile[BDIMY][BDIMX+IPAD];
//mapping from thread index to global memory offset
unsigned int idx=threadIdx.y*blockDim.x + threadIdx.x;
//shared memory store operation
tile[threadIdx.y][threadIdx.x]=idx;
syncthreads();
out[idx]=tile[threadIdx.x]threadIdx.y];
}

## Slide 35
Grid
공유메모리
(Shared Memory)
Register
Block 0
Register
Thread 0
Thread 1
공유메모리
(Shared Memory)
Register
Block 1
Register
Thread 0
Thread 1
Global Memory
Constant Memory
Texture Memory
Host
CUDA Memory Architecture

## Slide 36: Constant Memory
Constant Memory: A read-only special purpose memory accessible uniformly by threads in a warp.
It is read-only for kernels, the host can read and write it.
It is in device DRAM and has a dedicated on-chip cache whose size is 64KB per SM.
It is best if all threads in a warp access the same location in constant memory. Accesses to different addresses by threads within a warp are serialized.
Constant memory variable qualifier: It must be declared in global scope. It can be accessible from all threads within a grid and from the host through runtime functions.
__constant__

## Slide 37: constant memory variable initialization
cudaError_t cudaMemcpyToSymbol(const void *symbol, const void *src, size_t count, size_t offset, cudaMemcpyKind kind)
//copy the data pointed to by src to the constant memory location specified bt symbol on the device.

## Slide 38: constant memory example
P(x)=a0+a1x+a2x2+a3x3+a4x4
The coefficient a0~a4 are the same for all threads and never modified. These coefficients are excellent candidates for constant memory.

## Slide 39: Warp shuffle Instruction
The shuffle instruction was introduced for the architecture whose computer capability is 3.0 or higher such as Kepler, Maxwell families to allow threads to directly read another thread’s register as long as both threads are in the same warp.
The shuffle instruction therefore offers a way to interchange data among threads in a warp.

## Slide 40: lane in a warp
A lane : it simply refers to a single thread within a warp. A lane in a warp is identified by a lane index in the range [0,31].
In a 1D thread block, the laneID and warpID are obtained by the following realtions:
laneID=threadIdx.x%32,
warpID=threadIdx.x/32

## Slide 41: Warp Shuffle Instructions
Two sets of shuffle instructions: one for integer variables and one for float variables.
int __shfl(int var, int scrLane, int width=warpSize);
If every thread in a warp execute the following instruction:
int y = __shfl(x,5,16);
//thread0~thread15 get the value x from the thread 5 and thread16~thread31 get the value from the
thread21.

## Slide 42: int __shfl_up(), __shfl_down(), __shfl_xor
int __shfl_up(int var, unsigned int delta, int width=warpSize);
__shfl_up(val,2); //shift the value to the right two lane
int __shfl_xor(int var, int laneMask, int width=warpSize);
/*It calculates a source lane index by performing a bitwise XOR of the caller’s lane index with lane mask.
__shfl_xor(val,1); this instruction results in a butterfly exchange.

## Slide 43: examples of using the warp shuffling
Shuffle instruction can be applied to the three integer variable types:
Scalar variable,
Array,
Vector-typed variable.

## Slide 44: Homework#3( Due: April 13 )
The square matrices A,B and C have following relation:
C=A x B, where the column size is NY and row size is NX( in his case NX=NY).
The matrix multiplication in C is given below:
void matricMul( int *A, int *B, int *C, int size){
for(int col=0; col <size; col++){
for(int row=0; row <size; row++){
int outidx=col*size +row;
for( int idx=0; idx < size; idx++){
C[outidx] +=A[col*size+idx]*B[idx*size+row];}
}
}
}
Remark: A,B,C are square matrices represented in 1D row-major linear address memory.

## Slide 45: Matrix Multilication
Problem 1:
Make your CUDA program that uses only global memory on 2D grid and 2D blocks where:
int nx=15000;
int ny=15000;
int dimx=32;
int dimy=32;
dim3 block(dimx,dimy); //block dimension (32,32)
dim3 grid((nx + block.x-1)/block.x, (ny+block.y-1)/block.y);
Generate the matrix A and B treating them as linerar array:
//Data input
for( int i = 0; i < size; i++){
A[i] = i %1000; //input
B[i] = i %1000; // input
C[i] = 0;//output }

## Slide 46: Matrix Multiplication
Problem 2: Find out optimal block and grid size. Explain the reason.
Problem 3: Make your CUDA program with global and shared memory.
Compare and analyze your result with Problem 2.
Problem 4: Make your program of the Problem 3 removing all explicit memory copies between the host and the device and use the unified memory. Refer to the source code ‘sumMatrixGPUMaanaged.cu’ at Chap.4.
Explain the advantages and disadvantages of the usage of the unified memory
*At the host program, you have to implement the matrix multiplication code in C and compare the result from the device. If the result is same, your CUDA program is correct. You have to show the captured screen at your report.
* Use visual profiler as much as possible to show your result.

## Slide 47: Presentation Schedule on April 13
Mr. 한승열
Mr. 김영석
“CUDA-Accelerated Monte-Carlo for HPC
,Andrew Sheppard “
SC11, Seattle, WA 12-18 November 2011 .