## Slide 1
1. Binary System
Digital system – process data in a binary form, a system that manipulates discrete elements of
information represented internally in binary form
↑ signal (binary) –bit (binary digit)
discrete element

## Slide 2: Number System
Decimal number expression
representations of a number in a different radix are said to be equivalent if
they are the same decimal representation
decimal → number in base r
integer part & fraction part
integer part – ‘r’ 로 나누기
fraction part – ‘r’ 로 곱하기
a5a4a3a2a1a0.a-1a-2a-3
= anrn+an-1rn-1+...+a2r2+a1r+a0+a-1r-1+a-2r-2+...+a-mr-m
  7392 = 7 × 103 + 3 × 102 + 9 × 101 +2 × 100
  (11010.11)2 =1×24+1×23+0×22+1×21+0×20+1×2-1+1×2-2
  = (26.75)10
  (231.463)8 = 2×82+ 3×81+ 1×80+ 4×8-1+ 6×8-2+ 3×8-3
  6C7.3A= 6×162 + C×161 + 7×160 + 3×16-1 + A×16-2
Numbers | Radix(r) | Number Conventions
Binary | 2 | 0, 1
Octal | 8 | 0, 1, ..., 6, 7
Decimal | 10 | 0, 1, ...,, 7, 8, 9
Hexadecimal | 16 | 0, 1, ..., 8, 9, A, B, C, D, E, F

## Slide 3: Binary Number
Augend | 101101 | Minuend: | 101101 | Multiplicand: | 1011
Addend | +100111 | Subtrahend: | -100111 | Multiplier: | *101
sum | 1010100 | Difference: | 000110 |  | 1011
 |  |  |  |  | 0000
 |  |  |  |  | 1011
 |  |  |  | Product: | 110111

## Slide 4: Number Base Conversions
Ex 1-1) Convert decimal 41 to binary.
answer : (41)10 = (a5a4a3a2a1a0)2 = (101001)2
 | Integer Quotient |  | Remainder | Coefficient
41/2 = | 20 | + | ½ | a0 = 1
20/2 = | 10 | + | 0 | a1 = 0
10/2 = | 5 | + | 0 | a2 = 0
5/2 = | 2 | + | ½ | a3 = 1
2/2 = | 1 | + | 0 | a4 = 0
1/2 = | 0 | + | ½ | a5 = 1
Integer | Remainder
41 | 
20 | 1
10 | 0
5 | 0
2 | 1
1 | 0
0 | 1
Answer
=101001

## Slide 5: Number Base Conversions
Ex 1-2) Convert decimal 153 to octal.
Ex 1-3) Convert (0.6875)10 to binary.
153 | 
19 | 1
2 | 3
0 | 2 = (231)8
 | Integer |  | Fraction | Coefficient
0.6875*2 = | 1 | + | 0.3750 | a-1 = 1
0.3750*2 = | 0 | + | 0.7500 | a-2 = 0
0.7500*2 = | 1 | + | 0.5000 | a-3 = 1
0.5000*2 = | 1 | + | 0.0000 | a-4 = 1
Answer:(0.6875)10 = (0.a-1a-2a-3a-4)2 = (0.1011)2
until the fraction becomes 0 or until the number of digits has sufficient accuracy

## Slide 6: Number Base Conversions
Ex 1-4) Convert (0.513)10 to octal.
 | Integer |  | Fraction | Coefficient
0.513*8 = | 4 | + | 0.104 | a-1 = 4
0.104*8 = | 0 | + | 0.832 | a-2 = 0
0.832*8 = | 6 | + | 0.656 | a-3 = 6
0.656*8 = | 5 | + | 0.248 | a-4 = 5
Answer:(0.513)10 = (0.a-1a-2a-3a-4)2 = (0.4065)8
until the fraction becomes 0 or until the number of digits has sufficient accuracy

## Slide 7: Octal and Hexadecimal Numbers
( 10 110 001 101 011 . 111 100 000 110 )2 = (26153.7406)8
2 6 1 5 3 7 4 0 6
( 10 1100 0110 1011 . 1111 0010 )2 = (2C6B.F2)16
2 C 6 B F 2
hexa – easier to recognize

## Slide 8: Converting Between Base 16 and Base 2
(2C6B)16=( 10 1100 0110 1011 )2
2 C 6 B
Conversion is easy!
  Determine 4-bit value for each hex digit
Note that there are 24 = 16 different values of four bits
Easier to read and write in hexadecimal.
Representations are equivalent!

## Slide 9: Converting Between Base 16 and Base 8
(2C6B)16=( 10 1100 0110 1011 )2
2 C 6 B
(26153)8=( 10 110 001 101 011 )2
2 6 1 5 3
1.Convert from Base 16 to Base 2
2. Regroup bits into groups of three starting from right
3. Ignore leading zeros
4. Each group of three bits forms an octal digit.

## Slide 10: How to represent signed Numbers
Plus and minus sign used for decimal numbers
For computers, desirable to represent everything as bits.
Three types of signed binary number representations: signed magnitude, 1’s complement, 2’s complement.
In each case: left-most bit(MSB) indicates sign: positive (0) or negative (1).

## Slide 11: Number Representation
n-bits binary number
  MSB : singed(+;positive,0) or unsinged (-;negative,1)
  (n-1) bit :magnitude
  Maxim represent integers in the range
  -2n-1 <= N <= 2n-1-1
  Consider signed magnitude:
    000011002 = 1210
    100011002 = -1210

## Slide 12: Signed Binary Numbers
Ex) The number 9 represented in binary with eight bit
+9 : 00001001
-9 : 10001001 (signed-magnitude representation)
11110110 (signed-1’s-complement representation)
11110111 (signed-2’s-complement representation)

## Slide 13: Signed Binary Numbers
signed magnitude : + → - by changing only the sign bit in the MSB from 0 to 1
signed 1’s complement : by complementing all the bits including the sign bit
signed 2’s complement : signed 1’s complement + 1
complement method > magnitude method : separate handling of the sign and the magnitude is awkward in computer. so, complement is normally used

## Slide 14: Complements – Diminished Radix Complement
r’s complements of N is rn-N
(r-1)’s complements of N is (rn-1)-N
: r진법 n자리수의 N의 보수
r=10, r-1=9, 9’complements of N is (10n-1)-N
Ex) the 10’s complements of 567 is 1000 - 567 = 433
the 9’s complements of 567 is 999 - 567 = 432
For binary number, r=2, r-1=1
Ex) the 1’s complements of 00000011 is 11111111 - 00000011 = 11111100
the 2’s complements of 00000011 is 100000000 - 00000011 = 11111101
The one’s complement of a binary number involves inverting all bits.
The two’s complement of a binary number involves inverting all bits and adding 1
complement – simplify the subtraction operation , simplify the logical manipulation

## Slide 15: Signed Binary Numbers
Arithmetic Addition
- signed-magnitude system follows the rules of ordinary arithmetic.
- signed-complement system requires only addition.
Arithmetic Subtraction
(±A)-(+B) = (±A)+(-B)
(±A)-(-B) = (±A)+(+B)
signed-magnitude addition:
1. if the sign is same
1) we add the two magnitudes
2) give the sum the common sign
2. if the sign is different
1) larger magnitude – smaller magnitude
2) give the subtraction the larger number’s sign
+6 |  | 00000110 |  | -6 |  | 11111010
+13 |  | 00001101 |  | +13 |  | 00001101
+19 |  | 00010011 |  | +7 |  | 00000111
+6 |  | 00000110 |  | -6 |  | 11111010
-13 |  | 11110011 |  | -13 |  | 11110011
-7 |  | 11111001 |  | -19 |  | 11101101

## Slide 16: Complements – Addition with Complements
Using 1’s complement numbers, adding numbers is easy.
  Step 1: Add binary numbers
  Step 2: Add carry to low-order bit (=end-around carry (mean removing the end carry and adding 1 to the sum))
Let’s compute (-3)10 + (-4)10
1. 둘다 음수 일 때
(-M)+(-N) : + ( >= 기 때문에 항상 end-around carry 발생)
= = - (N+M)의 1’s complement
2. 양수 (M) + 음수 (-N)
1) M > N
M + = (M-N) + = M-N (M-N > 0이기 때문에 항상 end-around carry 발생)
2) M <= N
M + = (<= 항상 end-around carry 발생 x) (N-M)의 1’s complement
X = | 1100
1’s complement of Y = | +1011
Sum = | 10111
Add Carry= | 1
Final result = | 1000

## Slide 17: Complements – Addition with Complements
Using 2’s complement numbers, adding numbers is easy.
  Step 1: Add binary numbers
  Step 2: Ignore carry bit
  Let (-5)+5
1. 둘다 음수 일 때
(-M)+(-N) : + ( >= 기 때문에 항상 end-around carry 발생)
= = - (N+M)의 2’s complement
2. 양수 (M) + 음수 (-N)
1) M >= N
M + = (M-N) + = M-N (M-N >= 0이기 때문에 항상 end-around carry 발생)
2) M < N
M + = (<= 항상 end-around carry 발생 x) (N-M)의 2’s complement
X = | 1011
2’s complement of Y = | +0101
Sum = | 10000
Ignore Carry= | 
Final result = | 0000

## Slide 18: Complements – Subtraction with Complements
Using 1’s complement numbers, subtracting numbers is easy
  Step 1: Take 1’s complement of 2nd operand
  Step 2: Add binary numbers
  Step 3: Add carry to low order bit
Let compute 1210-110
X = | 01100
Y = | -00001
 | 01100
1’s complement add = | 11110
result = | 101010
Add carry | + 1 01011

## Slide 19: Complements – Subtraction with Complements
Using 2’s complement numbers, subtracting numbers is easy
  Step 1: Take 1’s complement of 2nd operand
  Step 2: Add binary numbers
  Step 3: Ignore carry bit
Let compute 1210-110
X = | 01100
Y = | +11111
result = | 101011
Ignore carry | 01011

## Slide 20: Complements –Overflow
Let’s compute (5)10 +(6)10.
  (5)10 = +(101)2 = (0101)2
  (6)10 = +(110)2= (0110)2
Adding these two 4-bit codes…
There is no carry bit and sign bit is seen to be one, indicating an incorrect result, which is what we expect (1011)2 = (11)10 but (1011)2 = -(5)10.
Let’s compute (-6)10 +(-7)10.
Adding these two 4-bit codes…
Discarding the carry bit , the sign bit is seen to be zero, indicating an incorrect result. (0011)2 = (3)10

## Slide 21: Complements –Overflow
If an addition operation produces a result that exceeds the range of the number system, overflow is said to occur.

## Slide 22: Binary Code-BCD code
decimal decimal
①↓ ③↓
computer – binary → binary
② operation (bcd 사용시 can directly operate)
bcd 사용시 ①,③에서의 convert가 더 간단해진다.(하지만 bit는 더 많이 차지)
- the 4-bit code for one decimal
(185)10 = (0001 1000 0101)BCD = (10111001)2
BCD Addition
- if the binary sum is greater or equal to 1010, we add 0110 to obtain the correct BCD
ex) 184 0001 1000 0100
+ 576 0101 0111 0110
0111←(carry) 10000 1010
0110 0110
760 0111 0110 0000
4 |  | 0100 |  | 4 |  | 0100 |  | 8 |  | 1000
+5 |  | +0101 |  | +8 |  | +1000 |  | +9 |  | +1001
9 |  | 1001 |  | 12 |  | 1100 |  | 17 |  | 10001
 |  |  |  |  |  | +0110 |  |  |  | +0110
 |  |  |  |  |  | 10010 |  |  |  | 10111

## Slide 23: BCD in signed 10’s complement
sign bit (MSB) + : 0000 - : 1001
signed 2’s omplement에서의 +/- 연산과 동일 (end carry 무시)
ex) 375 – 240 = 135
0 375 0000 0011 0111 0101
+ 9 760 1001 0111 0110 0000
1010 ←(carry) 1011 ←(carry) 1101 0101
0110 0110 0110
1 0000 0001 0011 0101
(end carry discard)

## Slide 24: Binary Code-Other Decimal Codes
weighted code : BCD(8421), 84-2-1, 2421
2421,excess-3 code : self-complement code : 9’s complement of a decimal number is obtained directly by chaining 1’s to 0’s and 0’s to 1’s (1’s complement in binary)
ex) <excess-3>
395 0110 1100 1000
604 1001 0011 0111
<2421>
395 0011 1111 1011
604 1100 0000 0100

## Slide 25: Binary Code-Gray Code
Binary code -> Gray code
Gray code -> Binary code
only one bit in the code group changes in going from one number to the next

## Slide 26: Binary Code- ASCII Character Code

## Slide 27: Binary Code ▶ Parity check
Error-Detecting Code
 | With even parity | With odd parity
ASCII A = 1000001 | 01000001 | 11000001
ASCII T = 1010100 | 11010100 | 01010100
In an odd-parity code, the parity bit is specified so that the total number of ones is odd.
In an even-parity code, the parity bit is specified so that the total number of ones is even.
error bit의 갯수가 odd일때만 detect 가능 (even일때는 불가능)

## Slide 28: Binary Storage and Registers
Registers – A register with n cells can store any discrete
quantity of information that contains n bits.
Register Transfer

## Slide 29: Binary Logic
Definition of Binary Logic (deals with variables that take an two discrete values and with operations that assume logical meaning)
Logic Gates

## Slide 30: Binary Logic