## Slide 1
2. Boolean Algebra and Logic Gates

## Slide 2: Outline
Review: Duality Principle
Design
  Min term & Sum of Product
  Max Term & Product of SUM
Boolean function: Representation, Canonical form
Mores gates: XOR,XNOR, NAND, NOR

## Slide 3: Principle of Duality
Dual of a statement S is obtained Principle of Duality
  By interchanging * and +
  By interchanging interchanging 0 and 1
Dual of (a*1)*(0+a’) = 0 is (a+0)+(1*a’) = 1

## Slide 4: Boolean Functions:Terminology
F(a,b,c) = a’bc + abc’ + ab + c
Variable
  Represents a value (0 or 1), Three variables: a, b, and c
Literal
  Appearance of a variable, in true or complemented form
  Nine literals: a’, b, c, a, b, c’, a, b, and c
Product term
  Product of literals, Four product terms: a’bc, abc’, ab, c

## Slide 5: Representations of Boolean Functions
English 1: F outputs 1 when a is 0 and b is 0, or when a is 0 and b is 1.
English 2: F outputs 1 when a is 0, regardless of b’s value
Equation 1: F(a,b) = a’b’ + a’b
Equation 2: F(a,b) = a’

## Slide 6: Boolean Algebra and Logic Gates
Basic Definitions
  1. Closure : A set S is closed with respect to a binary operator if, for every pair of elements of S, the binary operator specifies a rule for obtaining a unique elements of S.
  2. Associative law : (x*y)*z=x*(y*z) for all x,y,z∈S
  3. Commutative law : x*y=y*x for all x,y∈S
  4. Identity elements: for all x∈S, e*x=x*e=x
  ex) set of integers I={…, -3, -2, -1, 0, 1, 2, 3, …}, x+0=0+x=x
  5. Inverse : A set S having the identity elements
  (Boolean algebra does not have +,* inverse)
  for all x∈S , y∈S, x*y=e
  6. Distributive law : x*(y+z)=(x*y) + (x*z)
  x+(y*z)=(x+y) * (x+z)
  Boolean algebra is an algebra that deals with binary variables and
  logic operations
  Boolean function described by algebraic expression using binary
  variable & logic operation

## Slide 7: Basic Theorems and Properties of Boolean Algebra
Consensus (a) xy+x'z+yz = xy+x'z (b) (x+y)(x'+z)(y+z) =(x+y)(x'+z)
∪ = or = + , ∩ = and = *
1 = 전체 집합, 0 = 공집합
x + x`을 곱하거나, x*x1을 더해서 식을 간략화 한다.
dual

## Slide 8: Representation Conversion
Need to transition between boolean expression, truth table, and circuit (symbols).
Converting between truth table and expression is easy.
Converting between expression and circuit is easy.
More difficult to convert to truth table.
Truth
Table
Circuit
Boolean
Expression

## Slide 9: Boolean function
Operator precedence
1. Parentheses 2. NOT (’) 3. AND (•) 4. OR (+)
Boolean function

## Slide 10: Boolean Functions – Algebraic Manipulation
Ex 2-1) Simplify the following Boolean functions to a minimum number of literals.
1. x(x'+y) = xx' + xy = 0 + xy = xy.
2. x +x'y = (x+x')(x+y) = 1(x+y) = x + y.
3. (x+y)(x+y') = x + xy + xy' + yy' = x(1+y+y') = x.
4. xy + x'z + yz = xy + x'z + yz(x+x')
= xy + x'z + xyz + x'yz
= xy(1+z) + x'z(1+y)
= xy + x'z
5. (x+y)(x'+z)(y+z) = (x+y)(x'+z) : by duality from function 4.
(A + B + C)'= (A+x)' let B+C=x
= A'x' by theorem 5(a)(DeMorgan)
= A'(B+C)' substitute B+C=x
= A'(B'C') by theorem 5(a)(DeMorgan)
= A'B'C' by theorem 4(b)(associative)
=> (A+B+C+D+…+F)' = A'B'C'D'…F'
(ABCD…F)' = A' +B'+ C' + D' + … + F'

## Slide 11: Boolean Functions – Complement of a Function
Complement of a variable x is x’ (0⇒ 1 and 1⇒ 0)
The complement of a function F is F’ and is obtained from an interchange of 0’s for 1’s and 1’s for 0’s in the value of F
The dual of a function is obtained from the interchange of AND and OR operators and 1’s and 0’s
Finding the complement of a function F
  1. Applying DeMorgan’s theorem as many times as necessary
  2. complementing each literal of the dual of F

## Slide 12: Boolean Functions – Complement of a Function
Ex 2-2) Find the complement of the functions
F1=x'yz'+x'y'z, F2=x(y'z'+yz).
F1' = (x'yz'+x'y'z)' = (x'yz')'(x'y'z)' = (x+y'+z)(x+y+z')
F2' = [x(y'z'+yz)]' = x'+(y'z'+yz)' = x'+(y'z')'(yz)'
= x'+(y+z)(y'+z')
Ex 2-3) Find the complement of the functions F1 And F2 Ex 2-2 by taking their duals and complementing each literal.
1. F1 = x'yz' + x'y'z.
The dual of F1 is (x'+y+z')(x'+y'+z)
Complement each literal : (x+y'+z)(x+y+z')=F1'
2. F2 = x(y'z'+yz).
The dual of F2 is x+(y'+z')(y+z)이다.
Complement each literal : x'+(y+z)(y'+z')=F2'

## Slide 13: Canonical Form ‐‐ Sum of Minterms
Truth tables too big for numerous inputs
Use standard form of equation instead
  Known as canonical form
  Regular algebra: group terms of polynomial by power
    ax2 + bx + c (3x2 + 4x + 2x2 + 3 + 1 ‐‐> 5x2 + 4x + 4)
  Boolean algebra: create sum of minterms
    Minterm: product term with every function literal appearing exactly once, in normal (i.e., x) or complemented form (i.e., x’)
    Just multiply‐out equation until sum of product terms
    Then expand each term until all terms are minterms
Determine if F(a,b)=ab+a’ is same function as F(a,b) = a’ b ’+a’b+ab by canonical form.
  F = ab+a’ (already sum of products)
  F = ab + a’(b+b’) (expanding term)
  F = ab + a’b + a’b’ (it is canonical form)

## Slide 14: Canonical Form or Standard Form
Canonical forms
  Sum of minterms (SOM)
  Product of maxterms (POM)
Standard forms (may use less gates) → “회로 간략화＂
  Sum of products (SOP)
  Product of sums (POS)

## Slide 15: Minterms (standard product) → 곱이 항상 1
product term is a term where literals are ANDed.
  Example: x’y’, xz, xyz, …
Boolean variables can appear in normal (x) or complement form (x’)
Minterm : A product term in which all variables appear exactly once, in normal or complemented form
A minterm equals 1 at exactly one input combination and is equal to 0 otherwise
  Each AND combination of terms is a minterm
A minterm is denoted as mi where i corresponds the input combination at which this minterm is equal to 1

## Slide 16: Maxterms (standard sum) → 합이 항상 0
Sum term is a term where literals are ORed.
  Example: x’+y’, x+z, x+y+z, …
Boolean variables can appear in normal (x) or complement form (x’)
Maxterm : A sum term in which all variables appear exactly once, in normal or complemented form
A maxterm equals 0 at exactly one input combination and is equal to 1 otherwise
  Each OR combination of terms is a maxterm
A maxterm is denoted as Mi where i corresponds the input combination at which this minterm is equal to 0

## Slide 17: Minterms and Maxterms
Two variable minterms and maxterms.
• The index above is important for describing which variables in the terms are true and which are complemented.
index | Minterm | Maxterm
0 | x’ y’ | x+ y
1 | x’ y | x+ y’
2 | x y’ | x’+ y
3 | x y | x’+ y’

## Slide 18: Canonical and Standard Forms
complement

## Slide 19: Expressing Functions
Boolean function can be expressed algebraically from a give truth table
minterm & maxterm은 truth table에서 쉽게 얻을 수 있다.
function can be expressed algebraically as:
  The sum of minterms
  The product of maxterms
With Minterm
  ∑mi-For all the minterms that produce 1 in the function in the function
With Maxterm
  ΠMi-For all the maxterms that produce 0 in the function

## Slide 20: Example : minterm and maxterm

## Slide 21: Example(cont.)
Sum of Minterms
Ex ) Express the Boolean function F=A+B'C in a sum of minterms.
A = A(B+B') = AB +AB'
= AB(C+C') + AB'(C+C')
= ABC + ABC' + AB'C +AB'C'
B'C = B'C(A+A') = AB'C + A'B'C
F = A + B'C
= A' B'C + AB'C' + AB'C + ABC' + ABC
= m1 + m4 + m5 + m6 + m7
= ∑(1, 4, 5, 6, 7)

## Slide 22: Example(cont.)
Product of maxterms
Ex 2-5) Express the Boolean function F = xy + x'z in a product of maxterm form.
  F = xy + x'z = (xy+x')(xy+z)
  = (x+x')(y+x')(x+z)(y+z)
  = (x'+y)(x+z)(y+z)
  x' + y= x' + y + zz'= (x'+y+z)(x'+y+z')
  x + z= x + z + yy'= (x+y+z)(x+y'+z)
  y + z= y + z + xx'= (x+y+z)(x'+y+z)
  F = (x+y+z)(x+y'+z)(x'+y+z)(x'+y+z')
  = M0M2M4M5
  F(x, y, z) = ∏(0, 2, 4, 5)

## Slide 23: Example(cont.)
Ex) F = xy + x'z
F(x, y, z) = ∑(1, 3, 6, 7)
F(x, y, z) = ∏(0, 2, 4, 5)
F(A,B,C) = ∑(1,4,5,6,7)
↓ complement (F값이 1이 아닌 값들)
F`(A,B,C) = ∑(0,2,3)
↓ complement (minterm <-> maxterm)
F(A,B,C) = ∏(0,2,3)
F(A,B,C) = ∑(1,4,5,6,7) = ∏(0,2,3)
F을 sum of minterms & product of maxterms으로
모두 표현가능
mj` = Mj
maxterm with subscript j is a complement of the
minterm with the same subscript j and vice versa

## Slide 24: Canonical Forms
The sum of minterms and the product of maxterms forms are known as the canonical forms of a function

## Slide 25: Standard Forms
Sum of Products (SOP) and Product of Sums (POS) are also standard forms
  AB+CD = (A+C)(B+C)(A+D)(B+D)
The sum of minterms is a special case of the SOP form, where all product terms are minterms
The product of maxterms is a special case of the POS form, where all sum terms are maxterms
create two-level structure of gates (two-level structure produces the least amount of delay through the gates when the signal propagates from the inputs to the outputs)

## Slide 26: SOP and POS Conversion
SOP -> POS
F = AB + CD
= (AB+C)(AB+D)
= (A+C)(B+C)(AB+D)
= (A+C)(B+C)(A+D)(B+D)
POS -> SOP
F = (A’+B)(A’+C)(C+D)
= (A’+BC)(C+D)
= A’C+A’D+BCC+BCD
= A’C+A’D+BC+BCD
=A’C+A’D+BC

## Slide 27: Canonical and Standard Forms
Sum of Minterm  Product of Maxterm

## Slide 28: Standard Forms and Logic Circuit
Standard Forms
- Sum of product : F1 = y' +xy + x'yz'
- Product of sum : F2 = x(y'+z)(x'+y+z'+w)
Sum of products representation most common in industry.

## Slide 29: Other Logic Operations

## Slide 30: Digital Logic Gate

## Slide 31: Digital Logic Gate
excludes the combination of
both x and y being equal to 1

## Slide 32: Commutative/associative law
AND, OR, XOR, XNOR : both Commutative and associative law exist
NAND, NOR : only commutative law (should use the correct parentheses to signify the proper sequence of the gates)
the gate can be extended to have more than two inputs if the binary operation it represents is commutative and associative.
NAND, NOR – associative X → can’t be extended to have more than two input to overcome this difficulty
1. x↓y↓z (NOR) = (x+y+z)` (OR + complement)
2. x↑y↑z (NAND) = (xyz)` (AND + complement)
1,2을 이용해서 NOR, NAND의 multiple input을 표현한다.

## Slide 33: Digital Logic Gate
- exclusive-OR (XOR) :odd function

## Slide 34: Digital Logic Gate
Positive and Negative Logic