## Slide 1
Verilog HDL
• One of the two most popular languages
• Resembles C (remotely)
• Can represent logic diagrams, boolean
expressions, sequential circuits, modules etc
• Comes with a great variety of tools

## Slide 2
Brief History
• HDLs started in the early 80’s
• Became popular in the late 80’s
• There are two languages standardized by
IEEE: Verilog and VHDL
• Originally belonged to Cadence, now
controlled by Open Verilog Intl.

## Slide 3
Documentation Language
• Can be used to communicate designs
between humans
• Can be translated to/from schematic
diagrams
• Can be used to archive components for reuse

## Slide 4: Logic Simulation
Allows simulation at the logic level
Has a simple model for handling timing and delays
Has several primitives to facilitate simulation (for creating inputs and displaying outputs)
Test inputs are called test benches

## Slide 5: Logic Synthesis
From the HDL, create a list of components and their interconnections, called netlist
A netlist can be used to create anything from a silicon mask to a PCB
We will use HDLs program FPGA chips

## Slide 6: HDL(Hardware Description Language)
VHDL, Verilog HDL
Module Representation
//HDL Example 3-1
//Description of the simple circuit of Fig. 3-37
module smpl_circuit(A,B,C,x,y);
input A,B,C;
output x,y;
wire e;
and g1(e,A,B);
not g2(y, C);
or g3(x,e,y);
endmodule

## Slide 7
Delays
• It is usually enough to assume constant
delays in digital logic simulation
• In reality delays can vary depending on
many factors (but you have to be an
electrical engineer to make sense)
• The timescale is set with the (backquote)
timescale compiler directive

## Slide 8
Timescale
• The timescale directive is
– `timescale 1ns/100ps
• This means that the unit of measurement is 1
nanosec and the accuracy is .1 nanosec

## Slide 9: HDL(Hardware Description Language)
Gate Delays - `timescale 1ns/100ps
//HDL Example 3-2
//Description of circuit with delay
module circuit_with_delay (A,B,C,x,y);
input A,B,C;
output x,y;
wire e;
and #(30) g1(e,A,B);
or #(20) g3(x,e,y);
not #(10) g2(y,C);
endmodule
//HDL Example 3-3
//Stimulus for simple circuit
module stimcrct;
reg A,B,C;
wire x,y;
circuit_with_delay cwd(A,B,C,x,y);
initial
begin
A = 1'b0; B = 1'b0; C = 1'b0;
#100
A = 1'b1; B = 1'b1; C = 1'b1;
#100 $finish;
end
endmodule

## Slide 10
Boolean Expressions
●
Familiar boolean expressions can be
specified
–
–
–
AND is &
OR is |
NOT is ~

## Slide 11
Boolean Example
●
Let’ s define
–
–
x = A + BC + B’ D
y = B’ C + BC’ D’

## Slide 12: HDL(Hardware Description Language)
//HDL Example 3-4
//Circuit specified with Boolean equations
module circuit_bln (x,y,A,B,C,D);
input A,B,C,D;
output x,y;
assign x = A | (B & C) | (~B & C);
assign y = (~B & C) | (B & ~C & ~D);
endmodule
Boolean Expressions
- AND, OR, NOT => (&), (|), (~)
assign x = (A & B) | ~C);

## Slide 13
UDPs in Verilog
●
One can define new primitives and use them
like the built-in primitives
Use the keyword primitive instead of
module
They can have only one output
They are called User Defined Primitives
●
●
●

## Slide 14
Example UDP
●
Define a primitive that implements
–
crctp(x,y,z) = Sigma(0, 2, 4, 6, 7)
a table is contained between the keywords table
and endtable
●
We will use tables
–

## Slide 15: HDL(Hardware Description Language)
User-Defined Primitives (UDP)
//HDL Example 3-5
//User defined primitive(UDP)
primitive crctp (x,A,B,C);
output x;
input A,B,C;
//Truth table for x(A,B,C) = Minterms (0,2,4,6,7)
table
// A B C : x (Note that this is only a comment)
0 0 0 : 1;
0 0 1 : 0;
0 1 0 : 1;
0 1 1 : 0;
1 0 0 : 1;
1 0 1 : 0;
1 1 0 : 1;
1 1 1 : 1;
endtable
endprimitive
//Instantiate primitive
module declare_crctp;
reg x,y,z;
wire w;
crctp (w,z,y,z);
endmodule

## Slide 16: Wire Elements (Combinational logic)
The following are syntax rules when using wires:
1. wire elements are used to connect input and output ports of a module instantiation together with some other element in your design.
2. wire elements are used as inputs and outputs within an actual module declaration.
3. wire elements must be driven by something, and cannot store a value without being driven. In other words, wire elements are a stateless way of connecting two pieces in a Verilog-based design.
4. wire elements cannot be used as the left-hand side of an = or <= sign in an always@ block.
5. wire elements are the only legal type on the left-hand side of an assign statement.
6. wire elements can only be used to model combinational logic.

## Slide 17: Reg Elements (Combinational and Sequential logic)
The following are syntax rules when using wires:
1. reg elements can be connected to the input port of a module instantiation. Note that reg cannot connect to the output port of a module instantiation.
2. reg elements can be used as outputs within an actual module declaration. Note that reg cannot be used as inputs within an actual module declaration.
3. reg is the only legal type on the left-hand side of an always@ block = or <= sign.
4. reg is the only legal type on the left-hand side of an initial block = sign (used in Test Benches).
5. reg cannot be used on the left-hand side of an assign statement.
6. reg can be used to create registers when used in conjunction with always@(posedge Clock) blocks.
7. reg can, therefore, be used to create both combinational and sequential logic.

## Slide 18: Example
wire A , B ;
reg I , J , K ; // simple 1 -bit wide reg elements
reg[8:0] Wide ; // a 9 -bit wide reg element
always @ ( A or B ) begin
I = A | B ;

## Slide 19: When wire and reg Elements are Interchangeable
wire and reg elements can be used interchangeably in certain situations:
1. Both can appear on the right-hand side of assign statements and always@ block = or <= signs.
2. Both can be connected to the input ports of module instantiations