## Slide 1: This Lecture
Chapter 5: Synchronous Sequential Logic

## Slide 2
Sequential Circuits
There are two types of sequential circuits: Synchronous and Asynchronous

## Slide 3
Two major types: depending on timing of their signals
Asynchronous sequential circuits (see Chapter 9)
  The transition happens at any instant of time
  Do not use clock pulses. Change of internal state occurs when there is a change in input variables
    Instability problem: may become unstable at times
  Storage elements work as time-delay device
    May be regarded as a combinational circuit with feedback
Synchronous sequential circuits
  The transition happens at discrete instants of time
  The circuit responds only to pulses on particular inputs
  Storage elements are affected only with the arrival of each pulse
Types of Sequential Circuits

## Slide 4
Synchronous Sequential Circuits
The outputs can come either from the combinational circuit or from the flip-flops or both The flip-flops receive their inputs from the combinational circuit and also from a clock signal with pulse that occurs at fixed intervals of time
The flip-flop outputs cannot change and the feedback loop is broken when a clock pulse is not active

## Slide 5
Flip-Flops
Sequential Circuits use flip-flops as storage elements
Flip-Flop is a binary storage device that saves one bit of information
The outputs can come from flip-flops or combinational logic
Flip-flop inputs come from combinational logic or clock generators

## Slide 6
Latches
Different flip-flops are different based on the number of inputs
and how the inputs affect the binary state.
Basic types of flip-flops operate with signal levels and are called latches.
Example: SR latch
Two states: Set and Reset states
an asynchronous sequential circuit with two cross-coupled NOR gates

## Slide 7
SR Latches
Two inputs labeled S for set and R for reset
(S,R)=(1,0): set (Q=1, the set state)
(S,R)=(0,1): reset (Q=0, the reset/clear state)
(S,R)=(0,0): normal condition
no operation, in either the set or the reset state
depending on which input was most recently at 1
(S,R)=(1,1): indeterminate state (Q=Q'=0)
consider (S,R) = (1,1) ⇒ (0,0)
unpredictable next state when both inputs return to 0
(depend on which input returns to 0 first)

## Slide 8
SR Latches with NAND Gates(S’-R’ Latch)
SR latch with two cross-coupled NAND gates
  0 signal to change its state
  (S,R)=(0,1): set (Q=1, the set state)
  (S,R)=(1,0): reset (Q=0, the reset/clear state) (S,R)=(1,1): normal condition
  (S,R)=(0,0): indeterminate state (Q=Q’=1)
    unpredictable next state

## Slide 9
SR Latches with Control input
Determines when the state of the latch can be changed
C=0 ⇒ quiescent condition, no change
C=1 ⇒ S or R is allowed to affect the SR latch (1 signal to change its state)

## Slide 10
D Latch
S=D and R=D’
  Ensure S and R are never equal to 1 at the same time
  Eliminate the undesirable conditions of the indeterminate state in the SR latch
One output Q and two inputs: D (data) and C (control)
  Q = D when C=1
  Q = no change when C=0.
Also called a transparent latch
1
1
1
1
0
1
0
0
1
1

## Slide 11
Diagrams, Function Tables, and Graphic Symbols for Latches

## Slide 12
Flip-Flips
A trigger: the momentary change to switch the state of a latch or flip-flop
  The transition it causes is said to trigger the flip-flop
Types of triggers
  Level triggered – latches
  D latch is triggered every time the pulse stays at logic 1 level.
  Be used as a temporary storage between a unit and its environment
Edge triggered – flip-flops
  If level-triggered flip-flops are used, the feedback path may cause instability problem as long as the clock pulse stays in the active level
  triggered only during a signal transition (0⇒1 or 1⇒0)

## Slide 13
Flip-Flips
Many flip-flops are edge triggered:
They respond to the input only during transition from 0 to 1 or from 1 to 0.

## Slide 14
Edge-Triggered D Flip-Flop
1
1
0
1
Data blocked here while CLK =1
Store binary info during transition
Master-slave D flip-flop
two separate latch
a master latch (positive-level triggered)
a slave latch (negative-level triggered)
change only during negative edge of clock (1->0)
longer propagation delay

## Slide 15
Edge-Triggered D Flip-Flop
The output can change only when clock goes from 1 to 0.
0
1
1
1
Data passes here while CLK =0
1

## Slide 16
Positive Edge-Triggered D Flip-Flop
How is this a positive edge triggered? Lets look at all possible scenarios:
a) CLK = 0, then S=R=1 which causes the output to stay unchanged.
0
1
1

## Slide 17
Positive Edge-Triggered D Flip-Flop
How is this a positive edge triggered? Lets look at all possible scenarios:
a) CLK = 0, then S=R=1 which causes the output to stay unchanged.
0
1
1
Q=R ⇒

## Slide 18
Positive Edge-Triggered D Flip-Flop
What if CLK goes from 0 to 1? (↑ : Positive-edge) Q=D (state changes once)
a) D = 0, when CLK becomes 1, R changes 1 to 0. Flip-Flop goes to reset state. Q=0.
If D changes while CLK = 1, R remains 1. Q does not change.
1
0
1
1
1
1
1
S used to be 1 when CLK was 0
1
0
0
Since one input is 0 changes in D can’t change Q

## Slide 19
Positive Edge-Triggered D Flip-Flop
What if CLK goes from 0 to 1? (Positive-edge)
b) D = 1, when CLK becomes 1, S changes to 0. Flip-Flop goes to set state. Q=1.
If D changes while CLK = 1, R remains 0. Q does not change.
1
1
0
0
0
1
1
1
1
1
S and R used to be 1 when CLK was 0
1
1
1
0
0
Since one input is 0 changes in D can’t change Q

## Slide 20
Positive Edge-Triggered D Flip-Flop

## Slide 21
Setup Time and Hold Time
Setup time
  a minimum time for which the D input must be maintained at a constant value (or be ready) prior to the occurrence of the clock transition
  data to the internal latch
Hold time
  a minimum time for which the D input must not changes after the application of the positive transition of the clock
  clock to the internal latch

## Slide 22
Graphic Symbols

## Slide 23: Other Flip-Flops
Each flip-flop is made of interconnection of gates.
The edge-triggered D flip-flop is the most efficient flip-flop since it requires the least number of gates.
Other flip-flops are made using the D flip-flop and extra logic.
Two flip-flops widely used are the JK and T flip-flop.

## Slide 24: JK Flip-Flop
Three flip-flop operations: Set, Reset, Complement output.
JK performs all three

## Slide 25
JK Flip-Flop: D=JQ'+K'Q
J=0, K=0: D=Q ⇒ Q no change
J=0, K=1: D=0 ⇒ Q =0 reset to 0
J=1, K=0: D=1 ⇒ Q =1 set to 1
J=1, K=1: D=Q’ ⇒ Q =Q’ complement output
JK Flip-Flop

## Slide 26
T Flip-Flop
T (Toggle) flip-flop is a complementing one.
T flip-flop is obtained from a JK when inputs J and K are tied together.

## Slide 27
T Flip-Flop
If T=0 ( J=K=0) D=Q, output does not change.
If T=1 ( J=K=1) D=Q’ output is complemented.
A T flip-flop can also be made of D flip-flop and a XOR.
D = T ⊕ Q = TQ’ + T’Q

## Slide 28: Characteristic Tables
Characteristic equations
D flip-flop Q(t+1) = D
JK flip-flop Q(t+1) = JQ’+K’Q
T flop-flop Q(t+1) = T ⊕Q = TQ’ + T’Q

## Slide 29
Direct Inputs
Some flip-flops have asynchronous inputs to force the flip-flop to a particular state.
Examples: Direct Set, Direct Reset.
The input that sets the flip-flop to 1 is called preset or direct set.
The input that clears the flip-flop to 0 is called clear or direct reset.
Works independent of clock.

## Slide 30
Direct Inputs: Asynchronous Reset
Note reset signal for D flip flop
If R = 0, the output Q is cleared
This event can occur at any time, regardless of the value of the CLK

## Slide 31: Analysis of Clocked Sequential Circuits
Analysis: Obtaining a table/diagram for the time sequence of inputs/outputs/internal states.
Examples: State Equations, State Table, State Diagram

## Slide 32
Analysis of Clocked Sequential Circuits
Example of state equation:
A(t+1) = A(t)x(t) + B(t)x(t)
B(t+1) = A’(t)x(t)
A(t+1)=Ax+Bx
B(t+1)=A’x
y(t)=(A(t)+B(t)).x’(t)
= (A+B)x’

## Slide 33: Example of state tables
State equation:
A(t+1) = A(t)x(t) + B(t)x(t)
B(t+1) = A’(t)x(t) y(t)=(A(t)+B(t)).x’(t)
Sequence of outputs, inputs, and flip flop states enumerated in state table
Present state indicates current value of flip flops
Next state indicates state after next rising clock edge
Output is output value on current clock edge

## Slide 34: Example of state tables-2nd form
All possible input combinations enumerated
All possible state combinations enumerated
Separate columns for each output value.
Sometimes easier to designate a symbol for each state.

## Slide 35
Example of state diagram
Present state Next State Output
x=0 x=1 x=0 x=1
AB AB AB y y
00 00 01 0 0
01 00 11 1 0
10 00 10 1 0
11 00 10 1 0
Circles indicate current state
Arrows point to next state
For x/y, x is input and y is output
FIGURE 5.16 State diagram of the circuit of Fig. 5.15

## Slide 36
Analysis- D flip-flop
Note: this example
has no output

## Slide 37
Analysis: JK flip-flop
JA=B
KA=Bx’
J B=x’
KB=A’x+Ax’

## Slide 38
Analysis: JK flip-flop
A(t+1)=JA’+K’A
B(t+1)=JB’+K’B
A(t+1)=BA’+(Bx’)’A=A’B+AB’+Ax
B(t+1)=x’B’+(A XOR x’)B
=B’x’+ABx+A’Bx’

## Slide 39
Analysis: JK flip-flop
Present state input Next State
A B x A B
0 0 0 0 1
0 0 1 0 0
0 1 0 1 1
0 1 1 1 0
1 0 0 1 1
1 0 1 1 0
1 1 0 0 0
1 1 1 1 1

## Slide 40
Analysis: T flip-flop
Q(t+1)=T’Q+TQ’
TA=Bx
TB=x
y=AB
A(t+1)=(Bx)’A+(Bx)A’
=AB’+Ax’+A’Bx
B(t+1)=x XOR B

## Slide 41
Mealy Machine
Comb.
Logic
X(t)
Q(t+1)
Q(t)
Y(t)
clk
present
state
present
input
next
state
Comb.
Logic
Output based on state and present input
Asynchronous signals
Flip
Flops

## Slide 42
Moore Machine
Comb.
Logic
X(t)
Q(t+1)
Q(t)
Y(t)
clk
present
state
present
input
next
state
Comb.
Logic
Output based on state only
Outputs change synchronously with state changes
Flip
Flops

## Slide 43: Mealy versus Moore

## Slide 44: State Diagram with One Input & One Mealy Output
Mano text focuses on Mealy machines
State transitions are shown as a function of inputs and current outputs.
S1
S2
S3
S4
1/0
1/0
1/0
1/1
Input(s)/Output(s) shown in transition
0/0
0/0
e.g. 1
0/0
0/0

## Slide 45: State Diagram with One Input & a Moore Output
Moore machine: outputs only depend on the current state
Outputs cannot change during a clock pulse if the input variables change
Moore Machines usually have more states.
No direct path from inputs to outputs
Can be more reliable

## Slide 46: Designing Finite State Machines
Six Step Process
1. Understand the statement of the Specification
2. Obtain an abstract specification of the FSM
(state table or state diagram)
3. Perform a state minimization
4. Perform state assignment
5. Choose FF types to implement FSM state register
and build excitation table
6. Combinational circuit minimization

## Slide 47: Example: Detect 3 Consecutive 1 inputs
State S0 : zero 1s detected
State S1 : one 1 detected
State S2 : two 1s detected
State S3 : three 1s detected
0
Note that each state has 2 output arrows
Two bits needed to encode state

## Slide 48: State Table for Sequence Detector
Sequence of outputs, inputs, and flip flop states enumerated in state table
Present state indicates current value of flip flops
Next state indicates state after next rising clock edge
Output is output value on current clock edge
Present
State
Next
State
A B x A B y
0 0 0 0 0 0
0 0 1 0 1 0
0 1 0 0 0 0
0 1 1 1 0 0
1 0 0 0 0 0
1 0 1 1 1 0
1 1 0 0 0 1
1 1 1 1 1 1
Output
Input
S0 = 00
S1 = 01
S2 = 10
S3 = 11

## Slide 49: Finding Expressions for Next State and Output Value
Create K-map directly from state table (3 columns = 3 K-maps)
Minimize K-maps to find SOP representations
Separate circuit for each next state and output value

## Slide 50: Circuit for Consecutive 1s Detector
Note location of state flip flops
Output value (y) is function of state
This is a Moore machine.

## Slide 51: Concept of the State Machine
Example: Odd Parity Checker
Assert output whenever input bit stream has odd # of 1's
State
Diagram
Symbolic State Transition Table
Encoded State Transition Table
Note: Present state and output are the same value
  Moore machine

## Slide 52: Concept of the State Machine
Example: Odd Parity Checker
Next State/Output Functions
NS = PS xor PI; OUT = PS
D FF Implementation
Timing Behavior: Input 1 0 0 1 1 0 1 0 1 1 1 0

## Slide 53
Mealy and Moore Machines
Solution 1: (Mealy)
0/0
Even
Odd
1/1
1/0
0/1
0
Even
1
1
0
Reset
[0]
Odd
[1]
Output
Input
Output
Input
Transition
Arc
Output is
dependent only
on current state
O/P is dependent
on current state and
input in Mealy
Solution 2: (Moore)
Mealy Machine: Output is associated with the state transition
- Appears before the state transition is completed (by the next clock pulse).
Moore Machine: Output is associated
with the state
Appears after the state transition
takes place.

## Slide 54: Vending Machine FSM
Step 1. Specify the problem
Deliver package of gum after 15 cents deposited
Single coin slot for dimes, nickels
No change
Design the FSM using combinational logic and flip flops

## Slide 55: Vending Machine FSM
Step 2. Map into more suitable abstract representation
Tabulate typical input sequences:
three nickels
nickel, dime
dime, nickel
two dimes
two nickels, dime
Draw state diagram:
Inputs: N, D, reset
Output: open

## Slide 56: Vending Machine FSM
Step 3: State Minimization

## Slide 57: Vending Machine FSM
Step 4. State Encoding
How many flip-flops are needed?

## Slide 58: Vending Machine FSM
Step 5. Chose FF type for implementation

## Slide 59: Vending Machine FSM
Step 6. Combinational circuit minimization(JK FF )

## Slide 60: Vending Machine FSM
Step 6. Combinational circuit minimization(D FF easiest to use)
K-map for Open
K-map for D0
K-map for D1
Q1 Q0
D N
Q1
Q0
D
N
Q1 Q0
D N
Q1
Q0
D
N
Q1 Q0
D N
Q1
Q0
D
N

## Slide 61
D Q
Q
R
D Q
Q
R
Q0
N
N
Q0
Q1
N
Q1
D
D0
D1
Q1
OPEN
D
CLK
CLK
Vending machine FSM implementation based on D flip-flops(Moore).
Q1
Q0
Reset
Reset
Minimized Implementation

## Slide 62: Summary
Finite state machines form the basis of many digital systems
Designs often start from clear specifications
Develop state diagram and state table
Optimize using combinational design techniques
Mealy or Moore implementations possible
  Can model approach using HDL.
Notes: credential:
bring a computer
die photo
wafer
:
This can be an hidden slide. I just want to use this to do my own planning.
I have rearranged Culler’s lecture slides slightly and add more slides. This covers everything he covers in his first lecture (and more) but may
We will save the fun part, “ Levels of Organization,” at the end (so student can stay awake): I will show the internal stricture of the SS10/20.
Notes to Patterson: You may want to edit the slides in your section or add extra slides to taylor your needs.