## Slide 1: Lecture 5 CUDA Memory Architecture
Kyu Ho Park
Mar. 14, 2017

## Slide 2
Grid
공유메모리
(Shared Memory)
Register
Block 0
Register
Thread 0
Thread 1
공유메모리
(Shared Memory)
Register
Block 1
Register
Thread 0
Thread 1
Global Memory
Constant Memory
Texture Memory
Host
CUDA Memory Architecture

## Slide 3: CUDA Memory Characteristics
Registers : RW a thread
Local Memory : RW a thread
Shared Memory : RW all threads in a block
Global Memory : RW all threads in a device(grid) and the host
Constant Memory : R all threads in a device and the host
Texture Memory : R all threads in a device and the host

## Slide 4: Registers
An automatic variable is a local variable which is allocated and deallocated automatically when program flow enters and leaves the variable's scope.
An automatic variable declared in a kernel without any other type qualifiers is stored in a register.
Arrays declared in a kernel may be stored in registers.
A kernel uses registers to hold frequently accessed thread-private variables.
Fermi: limit of 63 registers per thread,
Kepler: 255 registers per thread.

## Slide 5: Memory Hierarchy
Registers
Caches(Primary,Secondary)
Main Memory
Disk Memory
Fastest(~2ns)
Slowest( 1~6ms)
smallest
biggest
Speed
Size
(~4ns, ~30ns)
~220ns

## Slide 6: Locality of Memory Access
Temporal locality: If at one point a particular memory location is referenced, then it is likely that the same location will be referenced again in the near future
Spatial locality: If a particular memory location is referenced at a particular time, then it is likely that nearby memory locations will be referenced in the near future

## Slide 7: Local Memory
Local arrays referenced with indices whose values cannot be determined at compile time.
Large local structures or array that would consume too much register space.
Any variable that does not fit within the kernel register limit.
Local memory is actually a part of Global memory that has high latency and low bandwidth.

## Slide 8: Local Memory(LMem)
When too many registers are used,
too many local variables are used,or local variables are arrays, local memory is allocated.
LMem is actually a part of Global Memory(GMem).
compiler option: -maxrregcount=32
//it limits the number of registers 32 per thread.

## Slide 9: Shared Memory(SMem)
On Chip memory,
access speed is the same as the L1 cache,
the size is 16KiB per SM, and easily used by CUDA.
static allocation
__shared__ int a[1024];
dynamic allocation
extern __shared__ int b[ ];

## Slide 10: SMem Read/Write
__global__ void LoadStoreSharedMemory(int *In, int *Out)
{
__shared__ int SharedMemory[512];
SharedMemory[threadIdx.x]=In[threadIdx.x];
__syncthreads( );
Out[threadIdx.x]=SharedMemory[threadIdx.x];
__syncthreads();
}
int main()
{
…..
LoadStoreSharedMemory<<<1,512>>>(dev_In,dev_Out);
….
return 0;
}

## Slide 11: Synchronization
A synchronization barrier enables multiple threads to wait until all threads have all reached a particular point of execution before any thread continues.
CUDA allows threads in the same block to coordinate their activities using a barrier synchronization function,
__syncthreads() .

## Slide 12: __syncthread()
A __syncthread() must be executed by all threads in a block. (they should __syncthread() at the same instruction address)
What will happen? ! not correct the instruction addres different!!!!!!
if( ) then{ A;
__syncthread();}
else {B;
__syncthread();}

## Slide 13: __syncthread()
The CUDA can execute blocks in any order relative each other because none of them must wait for each other.

## Slide 14: Global Memory(GMem)
GMem: DRAM at a Graphic Card.
GMem bandwidth: GPU uses 32Bytes,64Bytes or 128Bytes memory I/O.
GMem allocation and deallocation:
  cudaError_t cudaMalloc(void ** devPtr, size_t count);
  cudaErroe_t cudaFree(void* devPtr);
Memory copy
cudaError_t cudaMemcpy(void* dst, const void*src, size_t count, cudaMemcpyKind kind);

## Slide 15: Constant Memory(CMem)
CMem:
  some part of DRAM is used for CMem ,and it is read only and Cache is supported.
The max size is 64kB.
The host can write Cmem and the device can read it only.
All threads can share it like the global memory.
__constant__ int cData[6];
int hData[6] = {1,2,3,4,5,6};
cudaMemcpyToSymbol(“cData”,&hData,sizeof(hData));

## Slide 16: Texture Memory
It is in device memory and is cached in a per-SM, read-only cache.
Texture memory is a type of global memory that is accessed through a dedicated read-only cache.
It is optimized for 2D spatial locality.

## Slide 17: Texture
XX

## Slide 18: GPU Caches
L1
L2
Read-only constant
Read-only texture

## Slide 19: Global Variable
cudaMemcpyToSymbol(devData, &value, sizeof(float));
cudaMemcpyFromSymbol(&value, devData, sizeof(float));
-These are CUDA runtime API,
-devData is passed as a symbol,
-In the kernel, devData is used as variable in global memory.
The address of a global variable can be acquired by the CUDA API following;
float *dptr=NULL;
cudaGetSymbolAddress((void**)&dptr,devData);
cudaMemcpy(dptr, &value, sizeof(float),cudaMemcpyHostToDevice);

## Slide 20: Global Memory Allocation, Deallocation, Transfer
cudaError_t cudaMalloc(void **devPtr, size_t count);
cudaError_t cudaMemset(void *devPtr, int value, size_t count);
cudaError_t cudaFree(void *devPtr);
cudaError_t cudaMemcpy(void *dst, const void *src, size_t count, enum cudaMemcpyKind kind);

## Slide 21: CPU and GPU Memory
CPU
GPU Memory
CPU Memory
GPU
8GB/sec
144GB/sec
25GB/sec
pcie

## Slide 22: Pinned Memory
All host memory is pageable by default, since the host memory is managed by virtual memory system of OS.
The GPU cannot safely access data in pageable host memory because it has no control over when the host OS may choose to move that data.
To transfer data from pageable host memory to device memory, CUDA first allocates temporary page-locked (pinned) memory , copies the source host data to pinned memory and then transfers the data from pinned memory to device memory.

## Slide 23: Paging Model of Logical and Physical Memory
page 0
page 1
page 2
page 3
frame
number
logical
memory
0 | 1
1 | 4
2 | 3
3 | 7
page table
0 | 
1 | page 0
2 | 
3 | page 2
4 | page 1
5 | 
6 | 
7 | page 3
physical
address

## Slide 24: Pinned Memory

## Slide 25: Allocation of pinned host memory
cudaError_t cudaMallocHost(void **devPtr,size_t count);
Example:
cudaError_t status=cudaMallocHost((void**))&h_aPinned,bytes);
if(status !=cudaSuccess){
fprint(stderr,”Error returned from pinned host memory allocation\n”);
exit(1);}
//pinned memory release
cudaError_t cudaFreeHost(void *ptr);

## Slide 26: performance
memTransfer
pinMemTransfer

## Slide 27: Zero-Copy Memory
Between a host and the device,
Host cannot directly access device variables,
The device cannot directly access host variables.
In Zero-Copy Memory,
They provide ‘zero-copy memory’, and both the host and device can access it.

## Slide 28: Zero-Copy Memory
The host memory can be used when there is insufficient device memory,
Explicit data transfer is not necessary between the host and device,
Zero-copy memory is pinned(non-pageable)memory that is mapped into device address space.

## Slide 29: Zero-Copy Memory
cudaError_t cudaHostAlloc(void **pHost, size_t count, unsigned int flags); //Alocates ‘count’bytes of host memory that is page-locked and accessible to the device. the access speed is very slow because it use the pcie (the bandwidth of pcie is very slow than any device memory)
flags :
cudaHostAllocDefault
cudaHostAllocPortable :
cudaHostAllocWriteCombined
cudaHostAllocMapped : returns host memory that is mapped into device address space.

## Slide 30: Zero-Copy Memory
__global__ void sumArraysZeroCopy(float *A, float *B, float *C, const int N){
int i=blockIdx.x * blockDim.x + threadIdx.x;
if( i<N) C[i] = A[i] + B[i];
}
//Allocate A,B as zero-copy memory and C in device memory.

## Slide 31: Zero-Copy Memory

## Slide 32: Issues of Zero-Copy Memory
It simplifies programming.
For large data set shared by CPU and GPU that are connected by PCIe bus, it would be a poor choice.
There could be racing problem.

## Slide 33: Unified Virtual Addressing
CPU
GPU0
GPU1
CPU Memory
GPU0
Memory
GPU1
Memory
Introduced in CUDA 4.0
0
0x0000
0xFFFF

## Slide 34: Unified Memory (CUDA 6.0)
Managed memory refers to Unified Memory allocation that are automatically managed by the underlying system.
__device__ __managed__ int y;//This variable can be referenced directly from either host or device code.
cudaError_t cudaMallocManaged(void **devPtr, size_t size, unsigned int flags=0);//the host can use this.
This function allocates size bytes of managed memory and returns a pointer devPtr. The pointer is valid on all devices and the host.

## Slide 35: Memory Access Patterns
Most device data access begins in global memory, therefore the performance of GPU might be limited by the memory bandwidth.
Maximizing the use of global memory bandwidth is the fundamental step.

## Slide 36: Memory Hierarchy

## Slide 37: Memory Access
All accesses to global memory are through the L2 cache.
If L1 and L2 caches are used , a memory access is served by a 128-byte memory transaction.
If only L2 cache is used, a memory access is serviced by a 32-byte memory transaction. (disable L1 cache)
A L1 cache line is 128 bytes and it maps to a 128-byte aligned segment in device memory.
If each thread in a warp requests 4-byte value, that results in 128 bytes per request. It maps perfectly to the cache line size and device memory segment size.

## Slide 38: Two Characteristics of Memory Access
Aligned memory access:
The first address of a device memory transaction is an even multiple of the cache granularity, that is, 32-byte for
L2 cache or 128 bytes for L1 cache.
Coalesced memory access:
All 32 threads in a warp access a contiguous chunk of
memory.

## Slide 39: Aligned and Coalesced memory Access
128
256
Memory
threadId
0
31
threadId
0
31
misaligned and uncoalesced access
Memory Address

## Slide 40: Global Memory Reads
In an SM, 3 data paths:
1.L1/L2 cache
2.Constant cache
3.Read-only cache
L1 cache is enabled for global memory loads on Fermi devices and disabled on K40 and later GPUs.
Compiling with -Xptxas –dlcm=cg to disable L1.
Enabling L1: -Xptxas dlcm=ca
Explicit management needed

## Slide 41: Cached(L1) Load
L1-cached load operations are serviced at the granularity of an L1 cache line, 128-bytes.
Each thread requests a 4-byte at a time.

## Slide 42: Cached Loads
128
256
Addresses from a warp
Global memory
Aligned? Coalesced? How many memory transaction?

## Slide 43: Cached Loads
128
256
Addresses from a warp
Global Memory
Access is aligned and randomized within 128 bytes range.
How many 128-byte transaction is needed?

## Slide 44: Cached Loads
128
256
Addresses from a warp
Global memory
How many 128-bytes transactions are required?

## Slide 45: Cached Loads
128
256
Addresses from a warp
Global Memory
All threads in the request the same address.
Bus utilization?

## Slide 46: Cached Loads
128
256
Addresses from a warp
Global Memory
Threads in a warp request 32 four bytes addresses scattered all over the global memory.

## Slide 47: Uncached Loads
Uncached loads are performed at the granularity of 32-byte memory segments.
At compile time, use
-Xptas –dlcm=cg for L1 cache diabled.

## Slide 48: Uncached Loads
128
256
Addresses from a warp
Global Memory
Aligned and coalesced memory access
160
192
224

## Slide 49: Uncached Loads
128
256
Addresses from a warp
Global Memory
All threads in a warp requests 32 consecutive 4-bytes data. All accesses fall within 5 segments.
160
192
224
segment
64
96

## Slide 50: Uncached Loads
128
256
Addresses from a warp
Global Memory
All accsses request the same data.
160
192
224

## Slide 51: Misaligned Read
__global__ void readOffset(float *A, float *B, float *C, const int n, int offset) {
unsigned int i=blockIdx.x * blockDim.x + threadIdx.x;
unsigned int k= i + offset;
if( k<n) C[i] =A[k] + B[k];
}

## Slide 52: Global Load Efficiency gld_efficiency
gld_efficiency =
(Requested Global Memory Load Throughput)/
(Required Global Memory Load Throughput)

## Slide 53: $nvprof –metrics gld_transactions ./readSegment 0

## Slide 54: Global Memory Writes
L1 cache is not used for store operations.
L2 cache is used before being sent to device memory.
Store operation is performed at a 32-byte segment granularity.

## Slide 55: gst_efficiency
gst_efficiency: global store effriciency.
--global__ void writeOffset(float *A, float *B, float *C, const int n, int offset){
unsigned int i=blockIdx.x * blockDim.x + threadIdx.x;
unsigned int k=i+offset;
if(k<n) C[k]=A[i] + B[i];
}
$nvprof --metrics gst_efficiency --metrics gld_efficiency ./writeSegment 11
offset value

## Slide 56: Global Memory Writes
128
256
Addresses from a warp
Global Memory
Accesses are aligned and the addresses accessed are in a consecutive 64-byte(2 segments) range.
160
192
224

## Slide 57: Array of Structure , Structure of Array
Array of Structure(AOS)
struct innerStruct {
float x;
float y;
}
struct innerStruct myAoS[N];
Structure of Array(SOA)
struct innerArray{
float x[N];
float y[N];
}
struct innerArray mySOA;

## Slide 58: AOS and SOA
x | y | x | y | x | y | x | y | x | y
x | x | x | x | x | y | y | y | y | y
AOS Memory Layout
SOA Memory Layout
t0
t1
t2
t3
t4
t4
t2
t3
t1
t0

## Slide 59: Unrolling loops
__global__ void readOffset(float *A, float *B, float *C, const int n, int offset) {
unsigned int i=blockIdx.x * blockDim.x + threadIdx.x;
unsigned int k= i + offset;
if( k<n) C[i] =A[k] + B[k];
}
__global__ void readOffsetUnroll4(float *A, float *B, float *C, const int n,
int offset){
unsigned int i=blockIdx.x*blockDim.x *4 + threadIdx.x;
if(k+3*blockDim.x<n) {
C[i]=A[k];
C[i + blockDim.x] =A[k+blockDim.x] + B[k+blockDim.x];
C[i+ 2*blockDim.x]=A[k+2*blockDim.x]+B[k+2*blockDim.x];
C[i+ 3*blockDim.x]=A[k+3*block*Dim.x]+B[k+3*blockDim.x];
}
}

## Slide 60: Matrix Transpose
0 | 1 | 2 | 3
4 | 5 | 6 | 7
8 | 9 | 10 | 11
0 | 4 | 8
1 | 5 | 9
2 | 6 | 10
3 | 7 | 11
Matrix
Transposed Matrix

## Slide 61: Presentation Schedule 2 on 23 Mar., 2017
Mr. 기세환
Image Processing with CUDA, Jia Tse,2006.
Mr. 정휘영
Image Convolution with CUDA, Victor Podlozhnyuk, 2007.
  *Send your presentation file to
  TA Mr.Kim Woo Joong, PhD Student(w.j.kim@kaist.ac.kr) before your presentation to upload it to the Web.
*Homework#2 will be issued on 16 Mar. 2017