## Slide 1: Lecture 3 CUDA Execution Model
Kyu Ho Park
Mar. 7, 2017

## Slide 2: Memory Hierarchyand Thread-Block-Grid
GRID
Shared Memory
Thread(0,0)
Thread(1,0)
Thread(2,0)
Thread(3,0)
Block(0,0)
Global Memory
Host
cudaMalloc
cudaMemcpy
cudaMemset
cudaFree
Kernel
Device

## Slide 3
Grid
공유메모리
(Shared Memory)
Register
Block 0
Register
Thread 0
Thread 1
공유메모리
(Shared Memory)
Register
Block 1
Register
Thread 0
Thread 1
Global Memory
Constant Memory
Texture Memory
Host
CUDA Memory Architecture

## Slide 4: Thread-Block-Grid
Grid: All threads spawned by a single kernel launch are collectively called a grid.
All threads in a grid share the same global memory space.
Block: A thread block is a group of threads that can cooperate with each other.
Threads from different blocks cannot cooperate.

## Slide 5: Thread-Block-Grid & Core-SM-Device
Block
….
Grid
Software
Hardware
CUDA core
SM
Device
Thread

## Slide 6: warp
A warp refers to a collection of 32 threads that are woven together and get executed in a lockstep. Each thread in a warp executes the same instruction on a different data.

## Slide 7: a block and warps
..
warp
SM
a block

## Slide 8: Thread-Block-Grid Model
thread
block
grid

## Slide 9
A thread block in a grid share the same global memory space.
A thread block is a group of threads that can cooperate with each other using
  Block-local synchronization
  Block-local shared memory.
Threads from different blocks cannot cooperate.
Threads are indexed using that can be accessed within kernel functions
  blockIdx(block index within a grid)
  threadIdx(thread index within a block)

## Slide 10: Simultaneous Thread Processing of a GPU
G80 16 SMs , max 768 threads/SM
  768x16= 12,288 threads in parallel
GT200 30 SM, max 1,024 threads/SM
  1,024x30=30,720 threads in parallel
GTX 1080,
the most recent one(2016)

## Slide 11: CUDA block and 1-D thread
thread block
t0
threadIdx.x=0
t1
t2
t3
t4
t5
threadIdx.x=5
The thread index is represented by the given variable ‘threadIdx’.
kernel function:
__global__ void kernel<<<1,6>>>(int a, int b, int c);

## Slide 12: Thread-SP, Block-SM
………
thread block
DP: Double Precision Thread Processor

## Slide 13: __global__ void kernel<<<1,512>>>(int a, int b, int c);
thread0: threadIdx.x=0
thread1: threadIdx.x=1
….
thread511: threadIdx.x=511
G80: 16 SM

## Slide 14: __global__ void kernel<<<1,512>>>( )
Only one SM will be utilized and 15 SMs will be idle.
To utilize all SMs,
__global__ void kernel<<<16,32>>>( );

## Slide 15: threadIdx and blockIdx
threadIdx.x, threadIdx.y, threadIdx.z
blockIdx.x, blockIdx.y, blockIdx.z

## Slide 16: kernel<<<16,32>>> thread_indexing
block0 : threadIdx.x=0,…….,threadIdx.x=31
block1 : threadIdx.x=0,…….,threadIdx.x=31
…
block15: threadIdx.x=0,…….,threadIdx.x=31
int tid=blockIdx*blocDim.x + threadIdx.x;

## Slide 17
GT200: 30 SMs,
16SMs are active and 14 SMs are idle.

## Slide 18: Vector Sum
0 | 1 | 2 | 3 | . | . | . |  |  | 
0 | 1 | 2 | 3 | . | . | . |  |  | 
0 | 2 | 4 | 6 | . | . |  |  |  | 
+
=

## Slide 19: Vector Sum
#include <cuda.h>
#include <cuda_runtime.h>
#include <stdio.h>
__global__ void VectorAdd( int*a, int*b, int*c)
{
int tid = blockIdx.x * blockDim.x+ threadIdx.x;
c[tid] = a[tid] + b[tid];
}
int main()
{
const int size = 512*65535;
const int BufferSize = size*sizeof(int);
int* A;
int* B;
int* Sum;
//Allocation of the Host memory
A = (int*)malloc(BufferSize);
B = (int*)malloc(BufferSize);
Sum = (int*)malloc(BufferSize);
int i = 0;
//Data input
for( int i = 0; i < size; i++)
{
A[i] = i;
B[i] = i;
Sum[i] = 0;
}

## Slide 20
int* d_A; (gpu memory convention)
int* d_B;
int* d_Sum;
//Allocation of the Device memory
cudaMalloc((void**)&d_A, size*sizeof(int));
cudaMalloc((void**)&d_B, size*sizeof(int));
cudaMalloc((void**)&d_Sum, size*sizeof(int));
//Data transfer from the Host to the Device
cudaMemcpy(d_A, A, size*sizeof(int), cudaMemcpyHostToDevice);
cudaMemcpy(d_B, B, size*sizeof(int), cudaMemcpyHostToDevice);
//Add
VectorAdd<<<65535,512>>>(d_A, d_B, d_Sum);
//Device to Host
cudaMemcpy(Result, d_Sum, size*sizeof(int), cudaMemcpyDeviceToHost);
//Print out the result
for( i = 0; i < 5; i++){
printf(" Result[%d] : %d\n",i,Sum[i]);}
printf(" ......\n");
for( i = size-5; i < size; i++){
printf(" Result[%d] : %d\n",i,Sum[i]);}
cudaFree(d_A);
cudaFree(d_B);
cudaFree(d_Sum);
free(A);
free(B);
free(Sum);
return 0;
}

## Slide 21: __global__ void add()
__global__ void VectorAdd( int*a, int*b, int*c)
{
int tid = blockIdx.x * blockDim.x+ threadIdx.x;
c[tid] = a[tid] + b[tid];
}

## Slide 22: Thread-Block Dimension
blockDim: block dimension measured in threads.
A block is organized as a 3D array of threads.
gridDim: grid dimension measured in blocks.
Usually a grid is organized as a 2D array of blocks.
Any component left unspecified is initialized to 1
Host side : block.x block.y block.z grid.x grid.y grid.z
Device side : blockDim.x blockDim.y blockDim.z gridDim.x gridDim.y gridDim.z
Decide the block size
Calculate the grid dimension based on the application data size and the block size

## Slide 24: CUDA Thread-block-grid
1 block can have max. 1024 threads.
SM executes threads in a multiple of 32 threads.
__global__ void kernel<<<Dg,Db,Ns,S>>>();
Dg : dimension of the grid , type dim3.
Db : dimension of the block, type dim3.
Ns : number of bytes of shared memory which are dynamically allocated/block, type size_t.
S: Associated cudaStream_t. ‘S=0 ‘ means synchronous.

## Slide 25: thread-block dimensions
dim3 Dg(3,2,1);//(x,y,z) grid dimensions
dim3 Db(4,2,1);//(x,y,z) block dimensions
kernelFunction <<<Dg, Db>>> (a,b,c);
Grid
Block

## Slide 26: thread indexing
 |  |  |  |  |  |  |  | (tx,ty) |  |  | 
dim3 Dg(3,4,1);
dim3 Db(4,3,1);
int tid, tx,ty;
tx=blockDim.x*blockIdx.x + threadIdx.x;
ty=blockDim.y*blockIdx.y +
threadIdx.y;
tid=NX*ty+tx;
just think of the multidimensional array
int array [Ny][Nx] => IdxY*Nx + Nx
NX
NY
block

## Slide 27: Matrix Multiplication, PxQ=R
R(tx,ty)=P(0,ty)xQ(tx,0) + ... + P(11,ty)xQ(tx,11);
P
ty
R
txty
Q
ty

## Slide 28: Matrix Multiplication in C
void MatrixMulC( int*M, int*N, int*P, int Width)
{
int col = 0;
int raw = 0;
int index = 0;
int Destindex = 0;
for( col = 0; col < Width; col++)
{
for( raw = 0; raw < Width; raw++)
{
Destindex = col*Width+raw;
for( index = 0; index < Width; index++)
{
P[Destindex] += M[col*Width+index]*N[index*Width+raw];}}}}

## Slide 29: Matrix Multiplication
#include <cuda.h>
#include <cuda_runtime.h>
#include <stdio.h>
__global__ void MatrixMul( int*M, int*N, int*P, int Width)
{
int tid, tx, ty;
tx = blockDim.x*blockIdx.x + threadIdx.x;
ty = blockDim.y*blockIdx.y + threadIdx.y;
tid = Width*ty + tx;
int Value = 0;
int MVal = 0;
int NVal = 0;
for (int i = 0; i < Width; i++)
{
MVal = M[ty * Width + i];
NVal = N[i * Width + tx];
Value += MVal * NVal;
}
P[tid] = Value;
}

## Slide 30: Sample Program
int main()
{
const int MatrixWidth = 12;
const int MatrixHeight = 12;
const int MatrixSize = MatrixWidth*MatrixHeight;
const int BufferSize = MatrixSize*sizeof(int);
int* M;
int* N;
int* P_cuda;
int* P_C;
//Host memory allocation
M = (int*)malloc(BufferSize);
N = (int*)malloc(BufferSize);
P_cuda = (int*)malloc(BufferSize);
P_C = (int*)malloc(BufferSize);
int i = 0;
//Data input
for( int i = 0; i < MatrixSize; i++)
{
M[i] = i;
N[i] = i;
P_cuda[i] = 0;
P_C[i] = 0;
}
int* dev_M;
int* dev_N;
int* dev_P;
//Device memory allocation
cudaMalloc((void**)&dev_M, BufferSize);
cudaMalloc((void**)&dev_N, BufferSize);
cudaMalloc((void**)&dev_P, BufferSize);
//Host to device
cudaMemcpy(dev_M, M, BufferSize, cudaMemcpyHostToDevice);
cudaMemcpy(dev_N, N, BufferSize, cudaMemcpyHostToDevice);
dim3 Dg(3, 4, 1);
dim3 Db(4, 3, 1);
//Addition
MatrixMul<<<Dg,Db>>>(dev_M, dev_N, dev_P, 12);
//Device to Host
cudaMemcpy(P_cuda, dev_P, BufferSize, cudaMemcpyDeviceToHost);
MatrixMulC(M, N, P_C, 12);
bool ResultFlag = true;
//Print the result
for( i = 0; i < MatrixSize; i++)
{
//printf(" Result[%d] : %d, %d\n",i,P_cuda[i],P_C[i]);
if( P_cuda[i]!= P_C[i]) ResultFlag = false;
}
if( ResultFlag == true) printf(" MatrixMul Result OK!\n");
else printf(" MatrixMul Result Error!\n");
cudaFree(dev_M);
cudaFree(dev_N);
cudaFree(dev_P);
free(M);
free(N);
free(P_cuda);
free(P_C);
return 0;
}
I
II
III

## Slide 31: Warp

## Slide 32: Fast Context Switching

## Slide 33
Kernel
function0
Host
스레드
Kernel
function1
Device
Grid 0
Block
Block
Block
Block
스레드
스레드
스레드
Grid 1
Block
Block
Block
스레드
스레드
스레드
CUDA
Execution
Flow
One grid execution at a time on a device.
Different kernels may have different grid structures.

## Slide 34: Handling Errors
#define ERROR(function)
{
const cudaError_t error = function;
if( error !=cudaSuccess)
{
printf(“Error:%s, %d” , __FILE__,__LINE__);
printf(“code:%d, reason: %s\n”,error,cudaGetErrorsString(error));
exit(1);
}
}
Example:ERROR(cudaMemcpy(A, …….));

## Slide 35: Execution Time Check
CPU Timer
#include <sys/time.h>
Use ‘gettimeofday( )’ system call.

## Slide 36: Timing with nvprof
$nvprof ./hello
Time
107.23us…..
time for CPU,
time for cudaMemcpy
time for GPU…

## Slide 37: Organizing Parallel Threads
Matrix Addition:
  2D Grid with 2D Blocks
  1D Grid with 1D Blocks
  2D Grid with 1D Blocks

## Slide 38: Indexing Matrices with Blocks and Threads
An 8x6 matrix is stored linearly in global memory with a row-major approach.
ny=6
nx=8
row0 |  |  |  |  | row5
(0,0)…
…(7,5)
8x6 Matrix

## Slide 39: 2D Grid -2D Blocks
(ix,iy)
ix=threadIdx.x + blockIdx.x*blockDim.x
iy=threadIdx.y + bloxkIdx.y*blockDim.y
Global linear memory index, idx=iy*nx+ix

## Slide 40: Matrix with a 2D Grid and 2D Blocks
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
8 |  |  |  |  |  |  | 15
16 |  |  |  |  |  |  | 23
24 |  |  |  |  |  |  | 31
32 |  |  |  |  |  |  | 39
40 |  |  |  |  |  |  | 47
nx
ny
Block(0,0)
Block(1,0)
Block(0,1)
Block(1,1)
Block(0,2)
Block(1,2)
col 0
col 4
row 0
row 5

## Slide 41: Matrix with a 1D Grid and 1D Blocks
Block 0 | Block 1 | Block 2 | Block 3
nx
ny
idx=iy*nx + ix

## Slide 42: Matrix with a 2D Grid and 1D Blocks
Block(0,0) | Block(1,0) | Block(2,0) | Block(3,0)
Block(0,1) |  |  | 
Block(0,ny) | Block(1,ny) | Block(2,ny) | Block(3,ny)
idx=iy*nx + ix

## Slide 43: Homework#1
Due: Mar. 13, 2017
  To: Joo Kyung Ro, PhD Student(eu8198@kaist.ac.kr)
Page Limit of your report: max. 5pages excluding your source code and the screen captured result.

## Slide 44: hello.cu
#include <stdio.h>
__global__ void funct(void) {
printf(“Hello from GPU!\n”);
}
int main(void){
funct<<<1,4>>>( );
printf(“Hello, World from CPU!\n”);
cudaDeviceReset();
return 0;
}

## Slide 45: Problem 1
(1) Remove cudaDeviceReset() from the hello.cu and run it. Show the result and explain it.
(2) Replace cudaDeviceReset() in hello.cu with cudaDeviceSynchronize(). Run it and explain the result.
cudaDeviceSynchronize - A kernel call is asynchronous with respect to the host thread. After a kernel is invoked, control returns to the host side immediately. You can call the following function to force the host application to wait for all kernels to complete

## Slide 46: Problem 2- Addition of Matrices
At the page 19,20 of this lecture note, there is a sample program of vectors addition. Refer to the vector addition, make your program that add two matrices on 2D grid and 2D blocks where:
int nx=16384;
int ny=16384;
int dimx=32;
int dimy=32;
dim3 block(dimx,dimy); //block dimension (32,32)
dim3 grid((nx + block.x-1)/block.x, (ny+block.y-1)/block.y);
//grid dimension (512,512)
Generate the matrix A and B treating them as linear array as follows:
//Data input
for( int i = 0; i < size; i++)
{
A[i] = i;
B[i] = i;
Sum[i] = 0;
}

## Slide 47: Problem 2 continued
Run your program and measure the execution time using the Linux system call ‘gettimeofday()’.
Change the block configuration to
a. (32, 8), b. (32, 16), c. (32, 64),
d. (64, 8), e. (64, 16), f. (64, 32).
Compare and explain the execution time
of each case.

## Slide 48: Major Research Area of Students
Machine Learning and Its architectures:
강상훈,서준,Mario,김훈, 김혜지, 한승렬, Romain, 정휘영
1D,2D,3D Signal Processing
김용신,김영석,박진우,기세환,김태경
Parallel Processing
  배소윤,오은영,정재호,김재엽,유찬희
Others
이준희(SMS),박상욱(Security)

## Slide 49: Presentation Schedule
1.Mar. 16: 김태경
Matrix Multiplication with CUDA, Robert Hochberg, 2012.
2.Mar. 16: Romain Renard
Deep Learning Tutorial, Pater Sadowski,2015
or You may prepare the presentation material by yourself or
select some other material on the deep learning subject.