## Slide 1: Lecture 6 CUDA Global Memory
Kyu Ho Park
Mar. 21, 2017

## Slide 2: Performance Tuning
To optimize the bandwidth utilization of a device,
-Aligned and coalesced memory access,
-Sufficient concurrent memory operations are required.
To increase the concurrent memory access,
-Increasing the number of independent memory operations performed in each thread,
-kernel launch should be configured to get efficient parallelism.

## Slide 3: Parallelism
Task Parallelism:
It focuses on distributing functions across multiple cores.
Data Parallelism:
  It focuses on distributing the data across multiple cores.
  Data Partitions:
  1.Block Partition:
  Each thread takes one portion of data.
  2.Cyclic Partition:
  Each thread takes more than one portion
  of the data.

## Slide 4: Latency Hiding
Instruction Latency: the number of clock cycles between an instruction being issued and being completed.
Latency:
Arithmetic operations: 10~20 cycles
Global Memory Access: 400~800 cycles.

## Slide 5: Little’s Law
L = λW, where
λ : longterm average effective arrival rate,
W : average time a customer spends in the system.
Number of Required Warps
=Throughput x Latency.
In pipeline, L (operations) = λ (IPC) W (instruction latency)

## Slide 6: SM Parallelism Required to Maintain Full Arithmetic Utilization
GPU Model | Instruction Latency (Cycles) | Throughput (Operations/Cycle) | Parallelism (Operations)
Fermi | 20 | 32 | 640
Kepler | 20 | 192 | 3,830

## Slide 7: Device Parallelism Required to Maintain Full Memory Utilization
GPU Model | Memory Instruction Latency(Cycles) | Bandwidth (GB/Sec) | Bandwidth (Bytes/Cycle) | Parallelism (KB)
Fermi | 800 | 144 | 92 | 74
Kepler | 800 | 250 | 96 | 77
Fermi TeslaC2070: Memory frequency: 1.566GHz

## Slide 8: Unrolling a loop in C
//Normal Loop
int i;
for( i=0;i<100;i++)
{
function(i);
}
//Unrolled Loop
int i;
for( i=0; i<100; i+=4)
{
function( i );
function(i+1);
function(i+2);
function(i+3);
}
CVCV
number of compare reduces ¼
give 4 concurrency operation

## Slide 9: Advantage of the unrolling loop?
In the unrolled loop, the condition i<100 is only checked 25 times instead of 100 times.
The reads and writes performed in each statement of each loop are independent, the memory operations can be issued simultaneously by the CPU.
Unrolling in CUDA, more concurrent operations are added to the pipeline leading to higher saturation of instruction and memory bandwidth. This provides the warp scheduler with more eligible warps that can help hide instruction or memory latency.

## Slide 10: Perforemance Tuning:Unrolling loops
__global__ void readOffset(float *A, float *B, float *C, const int n, int offset) {
unsigned int i=blockIdx.x * blockDim.x + threadIdx.x;
unsigned int k= i + offset;
if( k<n) C[i] =A[k] + B[k];
}
__global__ void readOffsetUnroll4(float *A, float *B, float *C, const int n,
int offset){
unsigned int i=blockIdx.x*blockDim.x *4 + threadIdx.x;
unsigned int k = i + offset;
if(k+3*blockDim.x<n) {
C[i]=A[k] +B[k];
C[i + blockDim.x] =A[k+blockDim.x] + B[k+blockDim.x];
C[i+ 2*blockDim.x]=A[k+2*blockDim.x]+B[k+2*blockDim.x];
C[i+ 3*blockDim.x]=A[k+3*block*Dim.x]+B[k+3*blockDim.x];
}
}

## Slide 12: L1 cache enabled Performance

## Slide 13: Matrix Transpose
0 | 1 | 2 | 3
4 | 5 | 6 | 7
8 | 9 | 10 | 11
0 | 4 | 8
1 | 5 | 9
2 | 6 | 10
3 | 7 | 11
Matrix
Transposed Matrix

## Slide 14: Data Layout of Matrices
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11
0 | 4 | 8 | 1 | 5 | 9 | 2 | 6 | 10 | 3 | 7 | 11
original matrix ( can be aligned, coalesced O)
transposed matrix ( can be aligned, Coalesced X)
void transposeHost(float *out, float *in,const int nx, const int ny){
for(int iy=0; iy<ny; ++iy){
for(int ix=0; ix<nx;++ix){
out[ix*ny + iy]=in[iy*nx+ix];
}
}
}

## Slide 15
Read: by rows in the matrix, coalesced access.
Write: by columns in the transposed matrix, stride access which is the worst memory access pattern.
How to improve the bandwidth utilization:
Two approaches:
1.Read by rows and write by columns,
2.Read by columns and write by rows.

## Slide 16: read by row, write by column
Matrix
Transposed Matrix
ix
iy
(ix,iy)
nx
ny
iy
ny
nx
ix
(iy,ix)
ix=blockIdx.x*blockDim.x +
threadIdx.x,
iy=blockIdx.y*blockDim.y +
threadIdx.y

## Slide 17: Matrix Transpose
0 (0,0) | 1 (1,0) | 2 (2,0) | 3 (3,0)
4 (0,1) | 5 (1,1) | 6 (2,1) | 7 (3,1)
8 (0,2) | 9 (1,2) | 10 (2,2) | 11 (3,2)
0 (0,0) | 4 (0,1) | 8 (0,2)
1 (1,0) | 5 (1,1) | 9 (1,2)
2 (2,0) | 6 (2,1) | 10 (2,2)
3 (3,0) | 7 (3,1) | 11 (3,2)
Matrix
Transposed Matrix
(ix,iy)
(iy,ix)

## Slide 18: Transpose: Read in Row and Write in Column
__global__ void transposeRow(float *out, float *in, const int nx, const int ny){
unsigned int ix=blockDim.x*blockIdx.x+threadIdx.x;
unsigned int iy=blockDim.y*blockIdx.y+threadIdx.y;
if(ix < nx && iy<ny){
out[ix*ny + iy]= in[iy*nx + ix];
}
}

## Slide 19: read by column, write by row
Matrix
Transposed Matrix
ix
iy
(iy,ix)
nx
ny
iy
ny
nx
ix
(ix,iy)
iy=blockIdx.y*blockDim.y +
threadIx.y,
ix=blockIdx.x*blockDim.x +
threadIdx.x

## Slide 20: Matrix Transpose
0 (0,0) | 1 (0,1) | 2 (0,2) | 3 (0,3)
4 (1,0) | 5 (1,1) | 6 (1,2) | 7 (1,3)
8 (2,0) | 9 (2,1) | 10 (2,2) | 11 (2,3)
0 (0,0) | 4 (0,1) | 8 (0,2)
1 (1,0) | 5 (1,1) | 9 (1,2)
2 (2,0) | 6 (2,1) | 10 (2,2)
3 (3,0) | 7 (3,1) | 11 (3,2)
Matrix
Transposed Matrix
(iy,ix)
(ix,iy)

## Slide 21: Transpose Read by Column and Write by Row
__global__ void transposeCol(float *out, float *in, const int nx, const int ny){
unsigned int ix=blockDim.x*blockIdx.x+threadIdx.x;
unsigned int iy=blockDim.y*blockIdx.y+threadIdx.y;
if(ix < nx && iy<ny){
out[iy*nx + ix]= in[ix*ny + iy];
}
}

## Slide 22: Upper and Lower Performance Bound
Upper Bound (best, may be memory bandwidth): Copy the matrix by loading and storing rows, which are all coalesced accesses.
The number of memory operations is the same
as that of the matrix transpose.
Lower Bound (worst, may be memory bandwidth): Copy the matrix by loading and storing columns, which are all stride accesses.
The number of memory operations is the same
as that of the matrix transpose.

## Slide 24
cpu L1 : temporal & spatial locality
gpu L1 : spatial locality

## Slide 25: Unrolling Transpose
To improve the memory bandwidth of transpose, the unrolling transpose is to assign more independent work to each thread in order to maximize in-flight memory requests.

## Slide 26: Row-based unrolling
__global__ void transposeNaive4Row(float *out, float *in, const int nx, const int ny){
unsigned int ix=blockDim.x*blockIdx.x+threadIdx.x;
unsigned int iy=blockDim.y*blockIdx.y+threadIdx.y;
unsigned int ti=iy*nx+ix;
unsigned int to=ix*ny+iy;
if(ix+3*blockDim.x < nx && iy<ny){
out[to]= in[ti];
out[to+ny*blockDim.x]=in[ti+blockDim.x];
out[to+ny*2*blockDim.x]=in[ti+2*blockDim.x];
out[to+ny*3*blockDim.x]=in[ti+3*blockDim.x];
}
}

## Slide 27: Column-based Unrolling
__global__ void transposeNaive4Col(float *out, float *in, const int nx, const int ny){
unsigned int ix=blockDim.x*blockIdx.x+threadIdx.x;
unsigned int iy=blockDim.y*blockIdx.y+threadIdx.y;
unsigned int ti=iy*nx+ix;
unsigned int to=ix*ny+iy;
if(ix+3*blockDim.x < nx && iy<ny){
out[ti]= in[to];
out[ti+ny*blockDim.x]=in[to+blockDim.x];
out[ti+ny*2*blockDim.x]=in[to+2*blockDim.x];
out[ti+ny*3*blockDim.x]=in[to+3*blockDim.x];
} }

## Slide 28: Diagonal Transpose
(0,0) 0 | (1,0) 1 | (2,0) 2 | (3,0) 3
(0,1) 4 | (1,1) 5 | (2,1) 6 | (3,1) 7
(0,2) 8 | (1,2) 9 | (2,2) 10 | (3,2) 11
(0,3) 12 | (1,3) 13 | (2,3) 14 | (3,3) 15
int bid=blockIdx.y*gridDim.x + blockIdx.x;
Cartesian Coordinate

## Slide 29: Diagonal Transpose
(0,0) 0 | (0,1) 4 | (0,2) 8 | (0,3) 12
(1,3) 13 | (1,0) 1 | (1,1) 5 | (1,2) 9
(2,2) 10 | (2,3) 14 | (2,0) 2 | (2,1) 6
(3,1) 7 | (3,2) 11 | (3,3) 15 | (3,0) 3
Diagonal Coordinate
(blockIdx.x , blockIdx.y)
int bid=blockIdx.y*gridDim.x + blockIdx.x;
Transformation from the Diagonal Coordinate( blockIdx.x, blockIdx.y)
to the Cartesian Coordinate ( block_x, block_y):
block.x=(blockIdx.x+blockIdx.y)%gridDim.x;
block.y=blockIdx.x;

## Slide 30: Partition Camping
(0,0) 0 | (1,0) 1 | (2,0) 2 | (3,0) 3
(0,1) 4 | (1,1) 5 | (2,1) 6 | (3,1) 7
(0,2) 8 | (1,2) 9 | (2,2) 10 | (3,2) 11
(0,3) 12 | (1,3) 13 | (2,3) 14 | (3,3) 15
0 | 4 | 8 | 12
1 | 5 | 9 | 13
2 | 6 | 10 | 14
3 | 7 | 11 | 15
IN Data
OUT Data

## Slide 31: Partition Camping
Greg Ruetsch and Paulis Micikevicius,
“Optimizing Matrix Transpose in CUDA,”
NVIDIA.

## Slide 32: Diagonal Coordinate
0 | 4 | 8 | 12
13 | 1 | 5 | 9
10 | 14 | 2 | 6
7 | 11 | 15 | 3
0 | 13 | 10 | 7
4 | 1 | 14 | 11
8 | 5 | 2 | 15
12 | 9 | 6 | 3
IN Data
OUT Data

## Slide 33
Greg Ruetsch and Paulis Micikevicius,
“Optimizing Matrix Transpose in CUDA,”
NVIDIA.

## Slide 34: More Parallelism with Thin Blocks
nx
ny
ny
nx

## Slide 35: More Parallelism with Thin Blocks
Block Size | Bandwidth(GB/s)
(32,32) | 72.32
(32,16) | 51.46
(32,8) | 77.67
(16,32) | 113.04
(16,16) | 111.08
(16,8) | 82.01
(8,32) | 127.60
(8,16) | 112.59
(8,8) | 73.72
For the case ‘transposeNaiveCol’ with GTX970

## Slide 37: Presentation on Mar. 30, 2017
강상훈
NVIDIA Profiler User’s Guide, NVIDIA
김혜지
Greg Ruetsch and Paulis Micikevicius,
“Optimizing Matrix Transpose in CUDA,”
NVIDIA.