## Slide 1: Leakage reduction in instruction cache
Kim, Jinkwon
Embedded Computing Lab.
KAIST
Notes: Hi, my name is kim jin kwon, I am going to tell you leakage reduction in instruction cache

## Slide 2: Outline
Motivation
Terminology
  Leakage
reduction methods
  Gated-vdd
  Drowsy-cache
Observation
Implementation
Notes: This is outline about my presentation, first I will tell you motivation,terminology,methodology,observation,implemenation

## Slide 3: Motivation
Leakage power is Critical in chip power [1]
[1] Kim, Nam Sung, et al. "Leakage current: Moore's law meets static power." computer 36.12 (2003): 68-75.
Notes: This is my motivation.
the graph show the trend of the chip power consumption.
As you can see, leakage power is critical in chip power over time.

## Slide 4: Terminology
Leakage = static power
What is subthreshold leakage & gate leakage ?
[1] Li, Sheng, et al. "CACTI-P: Architecture-level modeling for SRAM-based structures with advanced leakage reduction techniques." Computer-Aided Design (ICCAD), 2011 IEEE/ACM International Conference on. IEEE, 2011.
Notes: You may ask me the question what is the leakage?
Leakage power is static power that consume your energy every second.
There are two major leakage in chip, first subthreshold leakage and gate leakage. in the picture, you can see that

## Slide 5: Reduction method
  Subthreshold power leakage reduction
    Gated-vdd : destroy the state, leakage reduction high, increase read time [1]
    Drowsy cache : state-preserving, leakage reduction low, need wake-up time [2]
[1] Powell, Michael, et al. "Gated-V dd: a circuit technique to reduce leakage in deep-submicron cache memories." Proceedings of the 2000 international symposium on Low power electronics and design. ACM, 2000.
[2] Kim, Nam Sung, et al. "Circuit and microarchitectural techniques for reducing cache leakage power." IEEE Transactions on Very Large Scale Integration (VLSI) Systems 12.2 (2004): 167-184.
Gated-vdd
Drowsy cache
Notes: Subthreshold power can be reduced by several methods. I tell you two famous method, one is gated-vdd , the other is drowsy cache.
Gated vdd can reduce the leakge reduction very high, but it destroy the state and increase read time and drowsy cache can preserve state, but leakage reduction is low.
I will choose the gated-vdd.

## Slide 6: Observation
Redundant instruction in the cache.
cmp r3,#0 | mov r7, #4 | mov r3,r0 | push {r4, lr}
ldr lr, [r3, #60] | cmp r3,#0 | sub r1, r1, #1 | mov r7, #4
pop {r4, pc} | mov r7, #4 | cmp r3,#0 | tst r2, #8
mov lr, #10 | mov r3,r1 | andeq r8, fp, r4, asr #19 | cmp r3,#0
Index
0
1
2
3
4
Notes: This is my observation.
I think there are some redundant instruction in the cache.
The picture show the simple direct instruction cache.
The red one and blue one show the redundant. red one repeat four times, blue one repeat three times.

## Slide 7: Observation
1. add small buffer that have original instruction
2. change from the redundant instruction to pointer that point the address in the buffer
3. cut the remain bit using gate-vdd
cmp r3,#0 pointer 0 | mov r7, #4 pointer 1 | mov r3,r0 | push {r4, lr}
ldr lr, [r3, #60] | cmp r3,#0 pointer 0 | sub r1, r1, #1 | mov r7, #4 pointer 1
pop {r4, pc} | mov r7, #4 pointer 1 | cmp r3,#0 pointer 0 | tst r2, #8
mov lr, #10 | mov r3,r1 | andeq r8, fp, r4, asr #19 | cmp r3,#0 pointer 0
Index
0
1
2
3
4
cmp r3,#0
mov r7,#4
Notes: My idea is that add small buffer that have original instruction.
And change from the redundant instruction to pointer that point the buffer address.
And then cut the reamin bit using gate-vdd

## Slide 8: Implementation
gem5 - to calculate the effect of buffer & redundant rate
Cacti - to calculate the energy & buffer access time & area overhead
Notes: Here is my implementation
I will use gem5 to calculate the effect of buffer and redundant rate and with cacti, I will calculate the energy & buffer access time & area overhead

## Slide 9
Any Questions?

## Slide 10
Reference
[1] Kim, Nam Sung, et al. "Leakage current: Moore's law meets static power." computer 36.12 (2003): 68-75
Li, Sheng, et al. "CACTI-P: Architecture-level modeling for SRAM-based structures with advanced leakage reduction techniques." Computer-Aided Design (ICCAD), 2011 IEEE/ACM International Conference on. IEEE, 2011.
Powell, Michael, et al. "Gated-V dd: a circuit technique to reduce leakage in deep-submicron cache memories." Proceedings of the 2000 international symposium on Low power electronics and design. ACM, 2000.
Kim, Nam Sung, et al. "Circuit and microarchitectural techniques for reducing cache leakage power." IEEE Transactions on Very Large Scale Integration (VLSI) Systems 12.2 (2004): 167-184.
Kaxiras, Stefanos, Zhigang Hu, and Margaret Martonosi. "Cache decay: exploiting generational behavior to reduce cache leakage power." ACM SIGARCH Computer Architecture News 29.2 (2001): 240-251.
Ye, Yibin, Shekhar Borkar, and Vivek De. "A new technique for standby leakage reduction in high-performance circuits." VLSI Circuits, 1998. Digest of Technical Papers. 1998 Symposium on. IEEE, 1998.
Yang, S., et al. "An integrated circuit/architecture approach to reducing leakage in deep-submicron high-performance I-caches." High-Performance Computer Architecture, 2001. HPCA. The Seventh International Symposium on. IEEE, 2001.