## Slide 1: Lecture 6 CUDA Global Memory
Kyu Ho Park
Mar. 21, 2017

## Slide 2: Performance Tuning
To optimize the bandwidth utilization of a device,
-Aligned and coalesced memory access, (memory bandwidth)
-Sufficient concurrent memory operations are required. (memory latency)
To increase the concurrent memory access,
-Increasing the number of independent memory operations performed in each thread,
-kernel launch should be configured to get efficient parallelism.

## Slide 3: Performance Tuning
Small threads per block exposes more parallelism to the GPU.
But when you have not enough thread per block, you can’t use the SM efficiently.
For example. Fermi GPU, the maximum number of concurrent blocks per SM is 8, and the maximum number of concurrent warps per SM is 48.
So, when you use 128 threads per block, there are 4 warps per block. So the maximum number of concurrent warps in the SM is 32 ! You can’t use the SM efficiently.

## Slide 4: Parallelism
Task Parallelism:
It focuses on distributing functions across multiple cores.
Data Parallelism:
  It focuses on distributing the data across multiple cores.
  Data Partitions:
  1.Block Partition:
  Each thread takes one portion of data.
  2.Cyclic Partition:
  Each thread takes more than one portion
  of the data.

## Slide 5: Latency Hiding
Instruction Latency: the number of clock cycles between an instruction being issued and being completed.
Latency:
Arithmetic operations: 10~20 cycles
Global Memory Access: 400~800 cycles.

## Slide 6: Little’s Law
L = λW, where
λ : longterm average effective arrival rate,
W : average time a customer spends in the system.
Number of Required Warps
=Throughput x Latency.
In pipeline, L (operations) = λ (IPC) W (instruction latency)

## Slide 7: SM Parallelism Required to Maintain Full Arithmetic Utilization
GPU Model | Instruction Latency (Cycles) | Throughput (Operations/Cycle) | Parallelism (Operations)
Fermi | 20 | 32 | 640
Kepler | 20 | 192 | 3,830

## Slide 8: Device Parallelism Required to Maintain Full Memory Utilization
GPU Model | Memory Instruction Latency(Cycles) | Bandwidth (GB/Sec) | Bandwidth (Bytes/Cycle) | Parallelism (KB)
Fermi | 800 | 144 | 92 | 74
Kepler | 800 | 250 | 96 | 77
Fermi TeslaC2070: Memory frequency: 1.566GHz

## Slide 9: Unrolling a loop in C
//Normal Loop
int i;
for( i=0;i<100;i++)
{
function(i);
}
//Unrolled Loop
int i;
for( i=0; i<100; i+=4)
{
function( i );
function(i+1);
function(i+2);
function(i+3);
}
CVCV
number of compare reduces ¼
give 4 concurrency operation

## Slide 10: Advantage of the unrolling loop?
In the unrolled loop, the condition i<100 is only checked 25 times instead of 100 times.
The reads and writes performed in each statement of each loop are independent, the memory operations can be issued simultaneously by the CPU.
Unrolling in CUDA, more concurrent operations are added to the pipeline leading to higher saturation of instruction and memory bandwidth. This provides the warp scheduler with more eligible warps that can help hide instruction or memory latency.

## Slide 11: Perforemance Tuning:Unrolling loops
__global__ void readOffset(float *A, float *B, float *C, const int n, int offset) {
unsigned int i=blockIdx.x * blockDim.x + threadIdx.x;
unsigned int k= i + offset;
if( k<n) C[i] =A[k] + B[k];
}
__global__ void readOffsetUnroll4(float *A, float *B, float *C, const int n,
int offset){
unsigned int i=blockIdx.x*blockDim.x *4 + threadIdx.x;
unsigned int k = i + offset;
if(k+3*blockDim.x<n) {
C[i]=A[k] +B[k];
C[i + blockDim.x] =A[k+blockDim.x] + B[k+blockDim.x];
C[i+ 2*blockDim.x]=A[k+2*blockDim.x]+B[k+2*blockDim.x];
C[i+ 3*blockDim.x]=A[k+3*block*Dim.x]+B[k+3*blockDim.x];
}
}

## Slide 13: L1 cache enabled Performance

## Slide 14: Matrix Transpose
0 | 1 | 2 | 3
4 | 5 | 6 | 7
8 | 9 | 10 | 11
0 | 4 | 8
1 | 5 | 9
2 | 6 | 10
3 | 7 | 11
Matrix
Transposed Matrix

## Slide 15: Data Layout of Matrices
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11
0 | 4 | 8 | 1 | 5 | 9 | 2 | 6 | 10 | 3 | 7 | 11
original matrix ( can be aligned, coalesced O)
transposed matrix ( can be aligned, Coalesced X)
void transposeHost(float *out, float *in,const int nx, const int ny){
for(int iy=0; iy<ny; ++iy){
for(int ix=0; ix<nx;++ix){
out[ix*ny + iy]=in[iy*nx+ix];
}
}
}

## Slide 16
Read: by rows in the matrix, coalesced access.
Write: by columns in the transposed matrix, stride access which is the worst memory access pattern.
How to improve the bandwidth utilization:
Two approaches:
1.Read by rows and write by columns,
2.Read by columns and write by rows.

## Slide 17: read by row, write by column
Matrix
Transposed Matrix
ix
iy
(ix,iy)
nx
ny
iy
ny
nx
ix
(iy,ix)
ix=blockIdx.x*blockDim.x +
threadIdx.x,
iy=blockIdx.y*blockDim.y +
threadIdx.y

## Slide 18: Matrix Transpose
0 (0,0) | 1 (1,0) | 2 (2,0) | 3 (3,0)
4 (0,1) | 5 (1,1) | 6 (2,1) | 7 (3,1)
8 (0,2) | 9 (1,2) | 10 (2,2) | 11 (3,2)
0 (0,0) | 4 (0,1) | 8 (0,2)
1 (1,0) | 5 (1,1) | 9 (1,2)
2 (2,0) | 6 (2,1) | 10 (2,2)
3 (3,0) | 7 (3,1) | 11 (3,2)
Matrix
Transposed Matrix
(ix,iy)
(iy,ix)

## Slide 19: Transpose: Read in Row and Write in Column
__global__ void transposeRow(float *out, float *in, const int nx, const int ny){
unsigned int ix=blockDim.x*blockIdx.x+threadIdx.x;
unsigned int iy=blockDim.y*blockIdx.y+threadIdx.y;
if(ix < nx && iy<ny){
out[ix*ny + iy]= in[iy*nx + ix];
}
}

## Slide 20: read by column, write by row
Matrix
Transposed Matrix
ix
iy
(iy,ix)
nx
ny
iy
ny
nx
ix
(ix,iy)
iy=blockIdx.y*blockDim.y +
threadIx.y,
ix=blockIdx.x*blockDim.x +
threadIdx.x

## Slide 21: Matrix Transpose
0 (0,0) | 1 (0,1) | 2 (0,2) | 3 (0,3)
4 (1,0) | 5 (1,1) | 6 (1,2) | 7 (1,3)
8 (2,0) | 9 (2,1) | 10 (2,2) | 11 (2,3)
0 (0,0) | 4 (0,1) | 8 (0,2)
1 (1,0) | 5 (1,1) | 9 (1,2)
2 (2,0) | 6 (2,1) | 10 (2,2)
3 (3,0) | 7 (3,1) | 11 (3,2)
Matrix
Transposed Matrix
(iy,ix)
(ix,iy)

## Slide 22: Transpose Read by Column and Write by Row
__global__ void transposeCol(float *out, float *in, const int nx, const int ny){
unsigned int ix=blockDim.x*blockIdx.x+threadIdx.x;
unsigned int iy=blockDim.y*blockIdx.y+threadIdx.y;
if(ix < nx && iy<ny){
int tid = iy*nx + ix;
int newX = tid%ny;
int newY = tid/ny;
out[newY*ny + newX]= in[newX*nx + newY];
}
}

## Slide 23: Which one is better?
Reads by rows and stores by columns
Reads by columns and stores by rows.
1) If L1 cache is disabled for loads
- these two implementations are theoretically identical!
2) If L1 cache is enable (L1 can be used in load but store)
- the second implementation should demonstrate better performance. While the reads performed by column will be uncoalesced (hence bandwidth will be wasted on bytes that were not requested), bringing those extra bytes into the L1 cache means that the next read may be serviced out of cache rather than global memory. Because writes are not cached in L1, the example that writes by column does not benefit from any caching

## Slide 24: Upper and Lower Performance Bound
Upper Bound (best, may be memory bandwidth): Copy the matrix by loading and storing rows, which are all coalesced accesses.
The number of memory operations is the same
as that of the matrix transpose.
Lower Bound (worst, may be memory bandwidth): Copy the matrix by loading and storing columns, which are all stride accesses.
The number of memory operations is the same
as that of the matrix transpose.

## Slide 26
cpu L1 : temporal & spatial locality
gpu L1 : spatial locality

## Slide 27: Unrolling Transpose
To improve the memory bandwidth of transpose, the unrolling transpose is to assign more independent work to each thread in order to maximize in-flight memory requests.

## Slide 28: Row-based unrolling
__global__ void transposeNaive4Row(float *out, float *in, const int nx, const int ny){
unsigned int ix=blockDim.x*blockIdx.x+threadIdx.x;
unsigned int iy=blockDim.y*blockIdx.y+threadIdx.y;
unsigned int ti=iy*nx+ix;
unsigned int to=ix*ny+iy;
if(ix+3*blockDim.x < nx && iy<ny){
out[to]= in[ti];
out[to+ny*blockDim.x]=in[ti+blockDim.x];
out[to+ny*2*blockDim.x]=in[ti+2*blockDim.x];
out[to+ny*3*blockDim.x]=in[ti+3*blockDim.x];
}
}

## Slide 29: Column-based Unrolling
__global__ void transposeNaive4Col(float *out, float *in, const int nx, const int ny){
unsigned int ix=blockDim.x*blockIdx.x+threadIdx.x;
unsigned int iy=blockDim.y*blockIdx.y+threadIdx.y;
unsigned int ti=iy*nx+ix;
unsigned int to=ix*ny+iy;
if(ix+3*blockDim.x < nx && iy<ny){
out[ti] = in[to]; out[ti + blockDim.x] = in[to+ blockDim.x*ny]; out[ti + 2*blockDim.x] = in[to+2*blockDim.x*ny]; out[ti + 3*blockDim.x] = in[to+3*blockDim.x*ny]; } }

## Slide 30: Diagonal Transpose
(0,0) 0 | (1,0) 1 | (2,0) 2 | (3,0) 3
(0,1) 4 | (1,1) 5 | (2,1) 6 | (3,1) 7
(0,2) 8 | (1,2) 9 | (2,2) 10 | (3,2) 11
(0,3) 12 | (1,3) 13 | (2,3) 14 | (3,3) 15
int bid=blockIdx.y*gridDim.x + blockIdx.x;
Cartesian Coordinate

## Slide 31: Diagonal Transpose
(0,0) 0 | (0,1) 4 | (0,2) 8 | (0,3) 12
(1,3) 13 | (1,0) 1 | (1,1) 5 | (1,2) 9
(2,2) 10 | (2,3) 14 | (2,0) 2 | (2,1) 6
(3,1) 7 | (3,2) 11 | (3,3) 15 | (3,0) 3
Diagonal Coordinate
(blockIdx.x , blockIdx.y)
int bid=blockIdx.y*gridDim.x + blockIdx.x;
Transformation from the Diagonal Coordinate( blockIdx.x, blockIdx.y)
to the Cartesian Coordinate ( block_x, block_y):
block.x=(blockIdx.x+blockIdx.y)%gridDim.x;
block.y=blockIdx.x;

## Slide 32: Partition Camping
(0,0) 0 | (1,0) 1 | (2,0) 2 | (3,0) 3
(0,1) 4 | (1,1) 5 | (2,1) 6 | (3,1) 7
(0,2) 8 | (1,2) 9 | (2,2) 10 | (3,2) 11
(0,3) 12 | (1,3) 13 | (2,3) 14 | (3,3) 15
0 | 4 | 8 | 12
1 | 5 | 9 | 13
2 | 6 | 10 | 14
3 | 7 | 11 | 15
IN Data
OUT Data

## Slide 33: Partition Camping
Requests to global memory are serviced by DRAM partitions.
Successive 256-byte regions of device memory are assigned to successive partitions. When using Cartesian coordinates to map thread blocks to data blocks, global memory accesses may not be evenly distributed among DRAM partitions, and a phenomenon called partition camping may occur.
In partition camping, memory requests are queued at some partitions while other partitions remain unused. Because the diagonal coordinate mapping causes non-linear mappings from thread blocks to the data blocks they process, strided accesses are unlikely to fall into a single partition, and performance improves as a result

## Slide 34: Partition Camping

## Slide 35: Diagonal Coordinate
0 | 4 | 8 | 12
13 | 1 | 5 | 9
10 | 14 | 2 | 6
7 | 11 | 15 | 3
0 | 13 | 10 | 7
4 | 1 | 14 | 11
8 | 5 | 2 | 15
12 | 9 | 6 | 3
IN Data
OUT Data

## Slide 36
Greg Ruetsch and Paulis Micikevicius,
“Optimizing Matrix Transpose in CUDA,”
NVIDIA.
diagonal coordinate
Read by row : use 3 partition each time
Write by column : use 3 partition each time
Cartesian coordinate
Read by row : use 3 partition each time
Write by column : use 1 partition each time

## Slide 37: More Parallelism with Thin Blocks
nx
ny
ny
nx

## Slide 38: More Parallelism with Thin Blocks
Block Size | Bandwidth(GB/s)
(32,32) | 72.32
(32,16) | 51.46
(32,8) | 77.67
(16,32) | 113.04
(16,16) | 111.08
(16,8) | 82.01
(8,32) | 127.60
(8,16) | 112.59
(8,8) | 73.72
For the case ‘transposeNaiveCol’ with GTX970
A “thin” block improves the effectiveness of store operations by increasing the number of consecutive elements stored by a thread block as a result of a larger value in the innermost dimension of the thread block. Matrix transpose할때의 경우

## Slide 40: Presentation on Mar. 30, 2017
강상훈
NVIDIA Profiler User’s Guide, NVIDIA
김혜지
Greg Ruetsch and Paulis Micikevicius,
“Optimizing Matrix Transpose in CUDA,”
NVIDIA.